## Slide 1: Basis of the BOLD signal
Ryan Oakeson & Helen Olawole-Scott
Expert: Nadine Graedel

## Slide 2: overview
MRI basics
  The MRI scanner
  Precession
  Excitation (Radio Frequency)
  T1, T2, T2* weighted images
  Gradient coils
BOLD signal
  Hemoglobin
  Hemodynamic response function (HRF)
  Magnetic susceptibility
  fMRI pros and cons
  fNIRS
  fNRIS pros and cons

## Slide 3: Magnetic Resonance imaging (MRI)
Non-invasive imaging method used for detection, diagnosis and treatment monitoring
MRI - uses spatial difference in resonance frequencies in different locations to form anatomical images
fMRI - uses magnetic properties of haemoglobin to create images illustrating changes in cortical blood flow
MRI strength between 1.5-7 tesla (**now 11.7T!**)
Scanner has many coils to produce different magnetic fields

## Slide 4: The benefits of water
72% water
Hydrogen atoms (protons) spin and have an overall positive charge
Net Magnetization Vector (M) = net direction of the protons’ magnetic fields in one unit of volume
Resonant characteristics
  Absorbing and re-radiating resonant (Larmor) frequency radiation
  Magnetic resonance (MR) signal

## Slide 5: What happens inside the scanner?
M = the net direction of the protons’ magnetic fields in one unit of volume
M

## Slide 6: Precession
Spins rotate or precess about an applied magnetic field, at the Larmor Frequency
  ω0 = γ Β0
  ω0 resonant frequency (e.g., 63.87 Hz for 1.5 T scanner)
  γ gyromagnetic ratio (42.58Hz for Hydrogen)
  Β0 magnetic field strength (1.5-7 T)
Precession frequency depends on the strength of the magnetic field

## Slide 7: Excitation - Radio Frequency (B1)
  The Radio Frequency (RF) transmitter introduces a second field – B1
  RF pulses knock the precessing protons in the transverse (X/Y) plane
  When RF pulses stop, protons precess back to their original alignment with B0, releasing the absorbed energy = MR signal
  Spin recovery (T1) – precession back towards B0 (longitudinal component o M)
  Phase decay (T2) – Dephasing of spins along the transverse component of M

## Slide 8: T1 weighted images
The T1 (i.e. the rate at which protons transfer energy to the environment) depends on tissue composition
MRI contrast is determined by the relaxation times as well as experimental timing (TE and TR)
T1-weighting is typically achieved using short repetition time, such that tissues are at different stages of T1-recovery when the RF pulse is played
Repetition times (TR) = is the amount of time between successive RF pulses applied to the same slice
Echo times (TE) = is the time between the delivery of the RF pulse and the receipt of the echo signal

## Slide 9: T2 weighted images
The RF pulse “knocks” the magnetisation vector M out of alignment with B0
The MRI signal measured is proportional to the length of the magnetization vector M in the transverse plane
Over time interactions between the spins mean they lose coherence and dephase, resulting in lower MRI signal.
This process is called T2-relaxation and is governed by the time-constant T2.
Like for T1, T2 is tissue-dependent and with appropriate choice of TE/TR T2-weighted images can be generated.
M
Dephasing

## Slide 10: T2* weighted images
Magnetic field inhomogeneities also cause dephasing
Time constant T2* describes signal decay caused by T2 as well as field inhomogeneities
T2* is defined as the time for the transverse component of the magnetisation to loose 63% of its value
T2* imaging is the contrast typically used in BOLD fMRI
M
Dephasing

## Slide 11: Gradient Coils give us Spatial Localisation
Gradient coils produce gradient magnetic field in X/Y/Z planes
Alter the strength of the primary magnetic field
Change the precession frequency of slices
Allows for spatial encoding for MRI images

## Slide 12: Any questions so far…?

## Slide 13: Basis of the BOLD signal

## Slide 14: Blood Oxygen-level Dependent
Part 1 – Hemoglobin and metabolism (Cerebral Metabolic Rate of O2)
  One of blood’s main functions is to deliver oxygen and nutrients through the body
  Much like the muscles in our body, neurons require oxygen to function
Part 2 – Hemodynamic response function and BOLD
  Oxygenated and deoxygenated blood have different magnetic properties
  This change in oxygenation and magnetic property in blood is the BOLD signaling
    Active vs resting contrasts

## Slide 15: Hemoglobin
Protein that contains iron in red blood cells which carry oxygen
Oxyhemoglobin (HbO2)
  Red
  Unstable bond
  Diamagnetic (less magnetic effect on its environment)
Deoxyhemoglobin (HbR)
  Blue/purple
  Paramagnetic (more magnetic effect on its environment)
Blood becomes deoxygenated due to increased metabolic processes involved in neural activation

## Slide 16
Resting
Active

## Slide 17: Hemodynamic Response Function (HRF)

## Slide 18
Interplay of:
CBF (cerebral blood flow)
CMRO2 (cerebral metabolic rate of oxygen)
CBV (cerebral blood volume)
Balloon model: CBV inflates venule during activation and the slowly deflates during the undershoot.

## Slide 19
Oxygenated and deoxygenated blood have different magnetic susceptibility
HbR is paramagnetic and causes a local field distortion
Bandettini and Wong, 1995
Oxyhemoglobin
  Diamagnetic
  less magnetic effect on its environment
  weak field inhomogeneities in high concentrations
  slower dephasing
Deoxyhemoglobin
  Paramagnetic
  more magnetic effect on its environment
  strong field inhomogeneities in high concentrations
  faster dephasing

## Slide 20: Impact Of Magnetic Susceptibility
HbO2 relaxes slower maintaining and has higher BOLD signal over time (less field distortion, longer T2*)

## Slide 21
This change in oxygenation and magnetic property in blood is the BOLD signaling
  Active vs resting contrasts
*At 3T

## Slide 22: fMRI Pros and Cons
High spatial resolution
Non-invasive
Not a direct measure of neural activity (BOLD signal)
Poor temporal resolution
Loud
Can’t have metal in or on body
Claustrophobic
Movement artifacts

## Slide 23: fNIRS (Functional Near-infrared Spectroscopy)

## Slide 24: fNIRS Pros and Cons
High temporal resolution
Low cost
Quiet
Less movement artifacts
Not a direct measure of neural activity (BOLD)
Poor spatial resolution
  Really only good for the cortex

## Slide 25: Thank you for listening! Any questions?