## Slide 1: Zurich SPM Course 2012 Spatial Preprocessing
Ged Ridgway, London
With thanks to John Ashburner
and the FIL Methods Group

## Slide 2: fMRI time-series movie
Notes: Auditory example data

## Slide 3: Preprocessing overview
REALIGN
COREG
SEGMENT
NORM WRITE
SMOOTH
ANALYSIS

## Slide 4: Preprocessing overview
fMRI time-series
Motion corrected
Mean functional
REALIGN
COREG
Anatomical MRI
SEGMENT
NORM WRITE
SMOOTH
TPMs
ANALYSIS
Input
Output
Segmentation
Transformation
(seg_sn.mat)
Kernel
(Headers changed)
MNI Space

## Slide 5: Reorientation and registration demo
Now to SPM…
… for more detail on things like mutual information, please see the May 2011 slides and/or my video at http://www.fil.ion.ucl.ac.uk/spm/course/video/

## Slide 6: B-spline Interpolation
B-splines are piecewise polynomials
A continuous function is represented by a linear combination of basis functions
2D B-spline basis functions of degrees 0, 1, 2 and 3
Nearest neighbour and trilinear interpolation are the same as B-spline interpolation with degrees of 0 and 1.

## Slide 7: Motion in fMRI
Is important!
  Increases residual variance and reduces sensitivity
  Data may get completely lost with sudden movements
  Movements may be correlated with the task
  Try to minimise movement (don’t scan for too long!)
Motion correction using realignment
  Each volume rigidly registered to reference
  Least squares objective function
Realigned images must be resliced for analysis
  Not necessary if they will be normalised anyway
Notes: Even tiny head movements can induce major artefacts in your data, so motion correction is very important.
-The t-test that is used by SPM (and that will be discussed in the next lecture) is based on the signal change relative to the residual variance. This signal is computed from the sum of squared differences between the data and the linear model to which it is fitted. Movement artefacts will add up to the residual variance and therefore reduce the sensitivity of your test.
-
-A lot of fMRI studies have paradigms in which the subject could be moving in a way that is correlated to the different experimental conditions, for example, when you would move your head each time you press a button. If you do not correct for this, these systematic differences might appear as activations in your data.

## Slide 8: Residual Errors from aligned fMRI
Slices are not acquired simultaneously
  rapid movements not accounted for by rigid body model
Image artefacts may not move according to a rigid body model
  image distortion, image dropout, Nyquist ghost
Gaps between slices can cause aliasing artefacts
Re-sampling can introduce interpolation errors
  especially tri-linear interpolation
Functions of the estimated motion parameters can be modelled as confounds in subsequent analyses

## Slide 9: fMRI movement by distortion interaction
Subject disrupts B0 field, rendering it inhomogeneous
  distortions occur along the phase-encoding direction
Subject moves during EPI time series
  Distortions vary with subject position
  shape varies (non-rigidly)

## Slide 10: Correcting for distortion changes using Unwarp
Estimate movement parameters.
Estimate new distortion fields for each image:
estimate rate of change of field with respect to the current estimate of movement parameters in pitch and roll.
Estimate reference from mean of all scans.
Unwarp time series.

+
Andersson et al, 2001

## Slide 11: Spatial Normalisation

## Slide 12: Spatial Normalisation - Reasons
Inter-subject averaging
  Increase sensitivity with more subjects
    Fixed-effects analysis
  Extrapolate findings to the population as a whole
    Mixed-effects analysis
Make results from different studies comparable by aligning them to standard space
  e.g. The T&T convention, using the MNI template

## Slide 13: Standard spaces
The MNI template follows the convention of T&T, but doesn’t match the particular brain Recommended reading: http://imaging.mrc-cbu.cam.ac.uk/imaging/MniTalairach
The Talairach Atlas
The MNI/ICBM AVG152 Template
Notes: Also DICOM scanner-based voxel-world mapping

## Slide 14: Normalisation via unified segmentation
MRI imperfections make normalisation harder
  Noise, artefacts, partial volume effect
  Intensity inhomogeneity or “bias” field
  Differences between sequences
Normalising segmented tissue maps should be more robust and precise than using the original images ...
… Tissue segmentation benefits from spatially-aligned prior tissue probability maps (from other segmentations)
This circularity motivates simultaneous segmentation and normalisation in a unified model

## Slide 15: Summary of the unified model
SPM8 implements a generative model
  Principled Bayesian probabilistic formulation
Gaussian mixture model segmentation with deformable tissue probability maps (priors)
  The inverse of the transformation that aligns the TPMs can be used to normalise the original image
Bias correction is included within the model

## Slide 16: Mixture of Gaussians (MOG)
Classification is based on a Mixture of Gaussians model (MOG), which represents the intensity probability density by a number of Gaussian distributions.
Image Intensity
Frequency

## Slide 17: Tissue intensity distributions (T1-w MRI)

## Slide 18: Non-Gaussian Intensity Distributions
Multiple Gaussians per tissue class allow non-Gaussian intensity distributions to be modelled.
  E.g. accounting for partial volume effects

## Slide 19: Modelling inhomogeneity
A multiplicative bias field is modelled as a linear combination of basis functions.
Corrupted image
Corrected image
Bias Field

## Slide 20: Tissue Probability Maps
Tissue probability maps (TPMs) are used as the prior, instead of the proportion of voxels in each class
ICBM Tissue Probabilistic Atlases. These tissue probability maps are kindly provided by the International Consortium for Brain Mapping, John C. Mazziotta and Arthur W. Toga.

## Slide 21: Deforming the Tissue Probability Maps
Tissue probability images are warped to match the subject
The inverse transform warps to the TPMs

## Slide 22: Optimisation
Find the “best” parameters according to an “objective function” (minimised or maximised)
Objective functions can often be related to a probabilistic model (Bayes -> MAP -> ML -> LSQ)
Value of parameter
Objective function
Global optimum (most probable)
Local optimum
Local optimum

## Slide 23: Optimisation of multiple parameters
Optimum
Contours of a two-dimensional objective function “landscape”

## Slide 24: Segmentation results
Tissue probability maps of GM and WM
Spatially normalised BrainWeb phantoms (T1, T2, PD)
Cocosco, Kollokian, Kwan & Evans. “BrainWeb: Online Interface to a 3D MRI Simulated Brain Database”. NeuroImage 5(4):S425 (1997)

## Slide 25: Spatial normalisation results
Non-linear registration
Affine registration

## Slide 26: Spatial normalisation – Overfitting
Template
image
Affine registration
(error = 472.1)
Non-linear
registration
without
regularisation
(error = 287.3)
Non-linear
registration
using
regularisation
(error = 302.7)
Without regularisation, the non-linear spatial normalisation can introduce unwanted deformation

## Slide 27: Spatial normalisation – regularisation
The “best” parameters according to the objective function may not be realistic
In addition to similarity, regularisation terms or constraints are often needed to ensure a reasonable solution is found
  Also helps avoid poor local optima
  Can be considered as priors in a Bayesian framework, e.g. converting ML to MAP:
    log(posterior) = log(likelihood) + log(prior) + c

## Slide 28: Spatial normalisation – Limitations
Seek to match functionally homologous regions, but...
  No exact match between structure and function
  Different cortices can have different folding patterns
  Challenging high-dimensional optimisation
    Many local optima
Compromise
  Correct relatively large-scale variability (sizes of structures)
  Smooth over finer-scale residual differences

## Slide 29: Smoothing
Why would we deliberately blur the data?
  Improves spatial overlap by blurring over minor anatomical differences and registration errors
  Averaging neighbouring voxels suppresses noise
  Increases sensitivity to effects of similar scale to kernel (matched filter theorem)
  Makes data more normally distributed (central limit theorem)
  Reduces the effective number of multiple comparisons
How is it implemented?
  Convolution with a 3D Gaussian kernel, of specified full-width at half-maximum (FWHM) in mm
Notes: Spatial normalisation is never exact, so homologous regions can never be precisely registered. Furthermore, due to the noisy nature of the BOLD signal, activations from different scans can be slightly offset, thereby cancelling each other out. Smoothing spreads out the different areas and reduces the discrepancy.

## Slide 30
Example of
Gaussian smoothing in one-dimension
A 2D Gaussian Kernel
The Gaussian kernel is separable we can smooth 2D data with two 1D convolutions.
Generalisation to 3D is simple and efficient
Notes: (A convolution is a kind of very general moving average.) First you convolve in one direction, than in the other two directions.
A general rule of thumb is to use a smoothing kernel of 6 mm for single subject analyses and a smoothing kernel of 8 or 10 mm when you are going to do a group analysis.

## Slide 31: References
Friston et al. Spatial registration and normalisation of images. Human Brain Mapping 3:165-189 (1995).
Collignon et al. Automated multi-modality image registration based on information theory. IPMI’95 pp 263-274 (1995).
Ashburner et al. Incorporating prior knowledge into image registration. NeuroImage 6:344-352 (1997).
Ashburner & Friston. Nonlinear spatial normalisation using basis functions. Human Brain Mapping 7:254-266 (1999).
Thévenaz et al. Interpolation revisited. IEEE Trans. Med. Imaging 19:739-758 (2000).
Andersson et al. Modeling geometric deformations in EPI time series. Neuroimage 13:903-919 (2001).
Ashburner & Friston. Unified Segmentation. NeuroImage 26:839-851 (2005).
Ashburner. A Fast Diffeomorphic Image Registration Algorithm. NeuroImage 38:95-113 (2007).

## Slide 32: Preprocessing overview
fMRI time-series
Motion corrected
Mean functional
REALIGN
COREG
Anatomical MRI
SEGMENT
NORM WRITE
SMOOTH
TPMs
ANALYSIS
Input
Output
Segmentation
Transformation
(seg_sn.mat)
Kernel
(Headers changed)
MNI Space

## Slide 33: Preprocessing (fMRI only)
fMRI time-series
Motion corrected
Mean functional
REALIGN
SEGMENT
NORM WRITE
SMOOTH
ANALYSIS
Input
Output
Segmentation
Transformation
(seg_sn.mat)
Kernel
MNI Space
TPMs

## Slide 34: Preprocessing overview
fMRI time-series
Motion corrected
Mean functional
REALIGN
COREG
Anatomical MRI
SEGMENT
NORM WRITE
SMOOTH
TPMs
ANALYSIS
Input
Output
Segmentation
Transformation
(seg_sn.mat)
Kernel
(Headers changed)
MNI Space

## Slide 35: Preprocessing with Dartel
fMRI time-series
Motion corrected
Mean functional
REALIGN
COREG
Anatomical MRI
SEGMENT
DARTEL NORM 2 MNI & SMOOTH
TPMs
(Headers changed)
ANALYSIS
DARTEL CREATE TEMPLATE
...