## Slide 1: SPM Course October 2019: Voxel-Based Morphometry
Dr Christian Lambert
Wellcome Centre for Human Neuroimaging, UCL

## Slide 2: INTRODUCTION

## Slide 3: What is VBM?
Voxel-Based Morphometry:
  Size and shape of the brain and its structures (“morphometry”)
  Compared at a voxel wise level across a population

## Slide 4: Examples applications of VBM
Many scientifically or clinically interesting questions might relate to changes in local volume of anatomical regions of the brain
For example, whether (and where) patterns of brain morphometry help to:
  Distinguish between groups (e.g. Alzheimer's vs. healthy controls)
  Explain changes seen in development and aging
  Identify plasticity, e.g. when learning new skills
  Find structural correlates (i.e. regions where the size correlates with scores, traits, genotype etc.,)

## Slide 5
Atrophy - AD vs. healthy
Controls (ADNI2 Dataset)
1. Phenotypic
patterns of disease
2. Ageing: GM
atrophy
Callaghan et al., 2014
3. Plasticity: Juggling
Scholz et al., 2009
4. Correlates: Political orientation
Kanai et al., 2011
Conservative - Decrease
Conservative - Increase

## Slide 6: Overview of SPM
Realignment
Smoothing
Normalisation
General linear model
Statistical parametric map (SPM)
Image time-series
Parameter estimates
Design matrix
Template
Kernel
Gaussian
field theory
p <0.05
Statistical
inference

## Slide 7: TISSUE SEGMENTATION

## Slide 8: Tissue segmentation for VBM
High-resolution MRI reveals fine structural detail in the brain, but not all of it reliable or interesting
  Noise, intensity-inhomogeneity, vessels
  MR Intensity is usually not quantitatively meaningful
  Quantitative MRI is possible though, and promising, see Voxel Based Quantification (VBQ) e.g. Draganski et al. (2011) PMID:21277375
Regional volumes of the three main tissue types: gray matter, white matter and CSF, are well-defined and potentially very interesting

## Slide 9: Tissue segmentation in SPM12 vs SPM8
SPM8 had a “New Segment” toolbox in addition to the main segmentation button
SPM8’s main segmentation has become the “Old Segment” toolbox in SPM12
SPM8’s New Segment provided the basis for SPM12’s segmentation, but there are several changes…
  New TPM.nii (from multispectral IXI database)
  Allowing rescaling of TPMs (like in Old Segment!)
  For full detail see SPM12 Release Notes and Appendix A in Malone et al. (2015) [PMID:25255942]

## Slide 10: Tissue segmentation in SPM12 vs SPM8
Evaluation of SPM12 versus SPM8 (Old) in terms of total intracranial volume, compared to manual tracing

## Slide 11: VOXEL BASED MORPHOMETRY

## Slide 12: Voxel-Based Morphometry
In essence VBM is Statistical Parametric Mapping of regional segmented tissue density or volume
The exact interpretation of gray matter density or volume is complicated, and depends on the preprocessing steps used
  It is not interpretable as neuronal packing density or other cytoarchitectonic tissue properties
  The hope is that changes in these microscopic properties may lead to macro- or mesoscopic VBM-detectable differences
  One technique is to use VBM in combination with other quantitative structural measures (diffusion, MT, R2*, SWI) to make biophysical inferences (example later)

## Slide 13: VBM: Step-by-step overview

## Slide 14
STEP 1!
** ALWAYS VISUALLY CHECK YOUR DATA**
Poor scan quality, artefacts, abnormal tissue (ischaemia, dural thickening), abnormal brains (hydrocephalus) relatively close rigid alignment (header issues)

## Slide 16: VBM overview
** ALWAYS VISUALLY CHECK YOUR DATA**
- Poor scan quality, artefacts, abnormal tissue (ischaemia, dural thickening), abnormal brains (hydrocephalus) relatively close rigid alignment (header issues)
Unified segmentation and spatial normalisation
  More flexible groupwise normalisation using DARTEL/Shoot
Modulation to preserve tissue volume
  Otherwise, tissue “density” (harder to interpret, registration errors)
  See also Radua et al. (2014) [PMID:23933042]
Optional computation of tissue totals/globals
Gaussian smoothing
Voxel-wise statistical analysis

## Slide 17: VBM in pictures
Segment
Normalise

## Slide 18: VBM in pictures
Segment
Normalise
Modulate
Smooth

## Slide 19: VBM in pictures
Segment
Normalise
Modulate
Smooth
Voxel-wise statistics

## Slide 20: VBM in pictures
Segment
Normalise
Modulate
Smooth
Voxel-wise statistics
beta_0001
con_0001
ResMS
spmT_0001
FWE < 0.05

## Slide 21: VBM SUBTLETIES
Modulation
How much to smooth
Interpreting results
Adjusting for total GM or Intracranial Volume
Statistical validity

## Slide 22: Modulation (“preserve amounts”)
Multiplication of warped (normalised) tissue intensities so that their regional total is preserved
  Can detect differences in completely registered areas
Otherwise, we preserve concentrations, and are detecting mesoscopic effects that remain after approximate registration has removed the macroscopic effects
  Flexible (not necessarily “perfect”) warping leaves less
1 1
2/3 1/3 1/3 2/3
1 1 1 1
Native
intensity = tissue probability
Modulated
Unmodulated
See also http://tinyurl.com/ModulationTutorial

## Slide 23
JACOBIAN DETERMINANT IMAGE (j_<image>.nii)

## Slide 24: Modulation (“preserve amounts”)
Top shows “unmodulated” data (wc1), with intensity or concentration preserved
  Intensities are constant
Below is “modulated” data (mwc1) with amounts or totals preserved
  The voxel at the cross-hairs brightens as more tissue is compressed at this point

## Slide 25: Smoothing
The analysis will be most sensitive to effects that match the shape and size of the kernel
The data will be more Gaussian and closer to a continuous random field for larger kernels
  Usually recommend >= 6mm
Results will be rough and noise-like if too little smoothing is used
Too much will lead to distributed, indistinct blobs (i.e. loss of spatial sensitivity)
  Usually recommend <= 12mm
Small subcortical nuclei (e.g. STN/SN) represent a special case where <<4mm may be warranted (see de Hollander et al., 2015)

## Slide 26: Smoothing
The results below show two fairly extreme choices
  5mm on the left, and 16mm on the right

## Slide 27: Smoothing as a locally weighted ROI
VBM > ROI: no subjective (or arbitrary) boundaries
VBM < ROI: harder to interpret blobs & characterise error

## Slide 28: Interpreting findings
Thickening
Thinning
Mis-classify
Mis-register
Mis-register
Contrast
Folding

## Slide 29: Adjustment for “nuisance” variables
Anything which might explain some variability in regional volumes of interest should be considered
  Age and gender are obvious and commonly used
    Consider age & age2 to allow quadratic effects
  Site or scanner if more than one (Note: model as factor, not covariate; multiple binary columns)
Total intracranial volume (TIV/ICV) often used for VBM
  Changes interpretation when correlated with local volumes (shape is a multivariate concept… See next slide)
  See also Barnes et al. (2010); Malone et al. (2015)

## Slide 30: VBM’s statistical validity
Residuals are not normally distributed
  Little impact for comparing reasonably sized groups
  Potentially problematic for comparing single subjects or tiny patient groups with a larger control group
    (Scarpazza et al, 2013; DOI: 10.1016/j.neuroimage.2012.12.045)
  Mitigate with large amounts of smoothing
  Or use nonparametric tests, e.g. permutation testing (SnPM)
    Though also not suitable for single case versus control group…
Smoothness is not spatially stationary
  Bigger blobs expected by chance in smoother regions
  NS toolbox http://www.fil.ion.ucl.ac.uk/spm/ext/#NS
Voxel-wise FDR is common, but not recommended

## Slide 31: NORMALISATION

## Slide 32: Spatial normalisation with DARTEL/Shoot
VBM is crucially dependent on registration performance
  The limited flexibility of DCT normalisation has been criticised
  Inverse transformations are useful, but not always well-defined
  More flexible registration requires careful modelling and regularisation (prior belief about reasonable warping)
  MNI/ICBM templates/priors are not universally representative
The DARTEL toolbox combines several methodological advances to address these limitations
  Voxel-wise DF, integrated flows, group-wise registration of GM & WM tissue segments to their (iteratively evolving) average

## Slide 33: DARTEL average template evolution
Rigid average (Template_0)
Average of mwc1 using segment/DCT
Template
6
Template
1
Notes: 60 images from OASIS cross-sectional data (as in VBM practical)

## Slide 34: Two diffeomorphic approaches in SPM
Dartel.
Uses the same small deformation composed multiple times.
Faster than Geodesic Shooting.
Gives similar deformations to Geodesic Shooting.
Currently more additional utilities.
Geodesic Shooting
Uses the optimal series of small deformations, which are composed together.
More mathematically correct than Dartel.
Gives nicer maps of volume change than Dartel.
Likely to replace Dartel in future.

## Slide 35: Group-wise alignment
Template implicitly generated from data in study.
Findings less biased by choice of template.

## Slide 36
471 Subject Average (DARTEL)

## Slide 37
471 Subject Average

## Slide 38
Subject 1

## Slide 39
471 Subject Average

## Slide 42
Part of Fig.1 in Klein et al.
Part of Fig.5 in Klein et al.

## Slide 43: Summary
VBM performs voxel-wise statistical analysis on smoothed (modulated) normalised tissue segments
SPM performs segmentation and spatial normalisation in a unified generative model
  Based on Gaussian mixture modelling, with warped spatial prior probability maps, and multiplicative bias field
Subsequent (non-unified) use of DARTEL or SHOOT toolboxes improves spatial normalisation for VBM
  (and probably also fMRI...)

## Slide 44: LONGITUDINAL ANALYSIS

## Slide 45: Longitudinal VBM – motivation
Development, growth, plasticity, aging, degeneration, and treatment-response are inherently longitudinal
Serial data have major advantages over multiple cross-sectional samples at different stages
Increasing power
  Subtlety of change over time vs. inter-individual variation
Reducing confounds
  Separating within-subject changes from cohort effects
  Demonstrating causality with interventions

## Slide 46: Longitudinal VBM – preprocessing
Intra-subject registration over time is much more accurate than inter-subject normalisation
Simple approach: rigid realignment within-subject
  Apply one spatial normalisation to all timepoints
  E.g. Draganski et al (2004) Nature 427: 311-312
More sophisticated approaches use nonlinear within-subject registration
  Information transferred to volume-change maps

## Slide 47: Longitudinal VBM – asymmetry & bias
Within-subject image processing often treats one time-point differently from the others
  Later scans registered (rigidly or non-rigidly) to baseline
Asymmetry can introduce methodological biases
  E.g. only baseline has no registration interpolation error
  Baseline seg. more accurate than propagated segs.
  Change in later intervals more regularised/constrained

## Slide 48: Longitudinal VBM – registration in SPM12
Ashburner & Ridgway (2013) [PMID: 23386806]
“Unified” rigid and non-rigid registration with model of differential intensity inhomogeneity (bias)
“Generative” – each time-point is a reoriented, spatially warped, intensity biased version of avg.
“Symmetric” with respect to permutation of images
“Consistent” with direct registration between pair
“Diffeomorphic” – complex warping without folding

## Slide 49: Longitudinal VBM – modelling
The longitudinal registration produces a within-subject average and maps of volume change relative to it
  Can perform cross-sectional VBM (Dartel, etc.) on averages
  Same spatial normalisation for volume-change maps
  Can multiply volume change with GM, then smooth
Simplest longitudinal statistical analysis: two-stage summary statistic approach (like in fMRI)
  Contrast on the slope parameter for a linear regression against time within each subject (usual group analyses of con images)
  For two time-points with interval approximately constant over subjects, equivalent to simple time2 – time1 difference image

## Slide 50
Timeyears
Subjects
T0
T1
T3
T4
Group Mean Template
Shoot
LVBM
Individual Longitudinal Templates
Longitudinal Analysis Model
Each individual is warped to their average
Each average template will be warped to a total group average
Each individual timepoint will produce diveregence & jacobian image
These can be used to calculate single “rate” maps
By repeating the segment-warp steps on the average images, VBQ-type analysis can be performed on the warped rate maps

## Slide 51: Longitudinal VBM – Getting started…
No longitudinal examples in SPM manual yet…
  Support on SPM list http://www.fil.ion.ucl.ac.uk/spm/support/
  Or email: ged.ridgway@gmail.com
The following slides illustrate usage of the longitudinal registration toolbox in the batch interface in SPM12

## Slide 52
No Longitudinal button, but found in Batch menu, like Dartel, etc.
Choice of paired or general serial.
No difference in model, but easier specification and results for pairs.

## Slide 53
Specify Time 1 scans for all subjects, then all Time 2 scans (in same order!)
Default values can be left; NaN to automatically estimate (Rician) noise
Vector (list) of time intervals (yr)

## Slide 54
One module per subject (scripting required if many subjects!)
Vector (list) of times relative to arbitrary datum (e.g. baseline=0)
Select all scans for this subject
Jacobian output useful to quantify interpretable ROI volumes (in litres)

## Slide 55
Output/results
  Average image
  Jacobians or divergences
  Deformations
Next steps
  Segment avg
  Run Dartel/Shoot
  Warp e.g. dv to standard space
  SPM stats on dv (TBM)
  Or combine with seg of avg (VBM)

## Slide 56
Timeyears
Subjects
T0
T1
T3
T4
Group Mean Template
Shoot
LVBM
Individual Longitudinal Templates

## Slide 57: Oasis Data
OAS2 0048
66 year old male, with MCI (MMSE=19, CDR=1).

## Slide 58: Oasis Data
Data from first 82 subjects (OAS2 0001 to OAS2 0099).
Computed average expansion/contraction rates for each subject.
Warped all data to common anatomical space.
Generated averages.
Mean image intensity
Control subjects
Dementia subjects

## Slide 60: WMH RATE
0.5
0
-0.5
“GROWTH”
“ATROPHY”

## Slide 62: Combining VBM with other measures
VBM provides a measure of voxel wise volumetric change.
In isolation, it can be tricky to infer underlying biophysical process i.e. what is driving volume change
Including additional quantitative MRI acquisitions in experimental design can augment this.
These can be analysed using “Voxel based Quantification” framework (very similar to VBM – see: Draganski et al. (2011) PMID:21277375)

## Slide 63: CONCLUSION
Introduced VBM & Potential uses
Tissue Segmentation
Statistics
VBM Subtleties
Normalisation via DARTEL/SHOOT
Longitudinal Toolbox
There is a lot more(!):
Quantitative MRI, Voxel based quantification, Cortical thickness analysis, lesion analysis, structural covariance, combining with multivariate machine learning techniques.. etc.,