## Slide 1: Voxel-Based Analysis of Quantitative Multi-Parameter Mapping (MPM) Brain Data for Studying Tissue Microstructure, Macroscopic Morphology and Morphometry
John Ashburner
Wellcome Trust Centre for Neuroimaging,
UCL Institute of Neurology,
London, UK.

## Slide 2: ROI Analyses
The most widely accepted way of comparing image intensities is via region of interest (ROI) analyses.
Involves manual placement of regions on images.
Compute mean intensity within each region.

## Slide 3: Automating ROI Analysis via Image Registration
If all images can be aligned with some form of template data, ROIs could be defined in template space.

## Slide 4: Automating ROI Analysis via Image Registration
These ROIs could then be projected on to the original scans.
Automatic.
  Less work.
  Repeatable.
Needs accurate registration.

## Slide 5: ROI Analysis via Spatial Normalisation
Alternatively, we could warp the images to the template space.
Use same ROI for each spatially normalised image.
This naïve approach does not give the same mean ROI intensity as projecting ROIs on to the original images.

## Slide 6: Expansion & Contraction
Deformations
Jacobian determinants

## Slide 7: Weighted Average
We can obtain the same results by using a weighted average.
Weight by Jacobian determinants.

## Slide 8: Weighted Average
Jacobian scaled warped images
Jacobian determinants

## Slide 9: Circular ROIs
Circlular ROIs in template space
Circlular ROIs projected onto original images

## Slide 10: Convolution
Original image
After convolving with circle

## Slide 11: Local Weighted Averaging
Jacobian scaled warped images
Jacobian determinants

## Slide 12: Local Weighted Averaging
Smoothed Jacobian scaled warped images
Smoothed Jacobians

## Slide 13: Compute the Ratio
Divide the smoothed Jacobian scaled data by the smoothed Jacobians.
Gives the mean values within circular ROIs projected onto the original images.
Ratio image

## Slide 14: Gaussian Weighted Averaging
We would usually convolve with a Gaussian instead of a circular function.
Ratio image
Gaussian kernel
Circular kernel

## Slide 15: Tissue-specific Averaging
Smoothed data contains signal from a mixture of tissue types.
Attempt to average only signal from a specific tissue type. Eg. White matter
JE Lee, MK Chung, M Lazar, MB DuBray, J Kim, ED Bigler, JE Lainhart, AL Alexander. A study of diffusion tensor imaging by tissue-specific, smoothing-compensated voxel-based analysis. NeuroImage 44(3):870-883, 2009.

## Slide 16: Tissue-specific Averaging
Original data
Tissue mask

## Slide 17: Masking the Data
Masked data
Tissue mask

## Slide 18: Jacobian Scaling and Warping
Jacobian scaled warped masked data
Jacobian scaled warped mask

## Slide 19: Smoothing
Smoothed scaled warped masked data
Smoothed scaled warped mask

## Slide 20: Compute the Ratio
Gives the local average white matter intensity.
Note that we need to exclude regions where there is very little WM under the smoothing kernel.

## Slide 21: Problems/Challenges
Needs very accurate image registration and segmentation.
  Signal intensity differences of interest will bias segmentation/registration.
Issues with partial volume
  White matter signal may be corrupted by grey matter at edges.
  Intensities dependent on surface area of interfaces.

## Slide 22: Some Other Approaches
JAD Aston, VJ Cunningham, MC Asselin, A Hammers, AC Evans & RN Gunn. Positron Emission Tomography Partial Volume Correction: Estimation and Algorithms. Journal of Cerebral Blood Flow & Metabolism 22(8):1019-1034, 2002. A framework to analyze partial volume effect on gray matter mean diffusivity measurements. NeuroImage 44(1):136-144, 2009.
TR Oakes, AS Fox, T Johnstone, MK Chung, N Kalin & RJ Davidson. Integrating VBM into the general linear model with voxelwise anatomical covariates. Neuroimage 34(2):500–508, 2007.
DH Salat, SY Lee, AJ van der Kouwe, DN Greve, B Fischl & HD Rosas. Age-associated alterations in cortical gray and white matter signal intensity and gray to white matter contrast. NeuroImage 48:21–28, 2009.
SM Smith, M Jenkinson, H Johansen-Berg, D Rueckert, TE Nichols, CE Mackay, KE Watkins, O Ciccarelli, MZ Cader, PM Matthews & TEJ Behrens. Tract-based spatial statistics: Voxelwise analysis of multi-subject diffusion data. NeuroImage 31(4):1487-1505, 2006.