## Slide 1: Basis of the BOLD signal
Physics and physiology
Louise McDonald and Yen Yu
24 November 2010
2010

## Slide 2: Aim
Explain physics of MRI and fMRI very simply
  Proton spin
  Magnets used in the scanner
  Image formation
  Contrasts, e.g. T1, T2, T2*
Only use essential terminology
A few numbers
Very few subscripts
NO EQUATIONS!!
2010

## Slide 3: History
1924 – Pauli suggested that atomic nuclei might spin and therefore have magnetic properties
1937 – Rabi showed that atomic nuclei (in gases) can absorb energy from magnetic fields = magnetic resonance (MR)
1945 – Purcell and Bloch demonstrated MR in solids and liquids
1972-1976 – Lauterbur and Mansfield’s work led to localisation of MR signals in 3D using echoplanar imaging
2010
Isidor Rabi
Nobel Prize 1944
Edward Purcell and Felix Bloch
Nobel Prize 1952
Paul Lauterbur and Peter Mansfield
Nobel Prize 2003

## Slide 4: History
1st MR image of a human body in 1977
2010
0.05T, 2 mins/voxel, 4h to get the image

## Slide 5: Protons and spin
Protons
  Hydrogen nuclei
  Very common in body tissue, which is about 80% water
Protons spin
  Usually in random directions
  Line up in magnetic fields
  Millions of protons in a typical voxel; 100,000 or more voxels in a brain scan
2010
Direction of
magnetic field
Proton spinning
(at rest)

## Slide 6: Proton spins
Proton spins are important
  At rest, the axes of the spins align with the static magnetic field
  After excitation, the axes of the spins precess about the magnetic field lines. (Precession frequency is 64MHz in a 1.5T magnetic field)
2010
Direction of
magnetic field (B0)
Proton spinning
(at rest)
Direction
of magnetic
field (B1)
Direction of
magnetic field (B0)

## Slide 7: What happens to protons in an MRI scan
When protons are at rest, MR signal cannot be detected
In order to detect an MR signal, you first need to excite the protons
  The RF transmitter coil generates a magnetic field (B1) at right angles to the static magnetic field (B0)
  The protons start to precess around the B1 magnetic field
  When the B1 magnetic field is switched off, protons gradually go back to where they were
  The relaxing protons emit a signal which can be detected by the RF receiver coil
Spin precession
  Following excitation, the frequency of the precession of the proton spins is determined by the strength of the magnetic field
  X, Y and Z gradient coils are used to apply gradients of magnetic field
  This changes the local spin precession frequency and is used to determine proton spin locations
A typical sequence consists of: excitation-apply gradients-measure signal
2010

## Slide 8: Magnets in the scanner
2010
RF receiver coil
4T magnet
Gradient coil
(inside)
Static magnetic field coil
Gradient coils
Shimming coil
Radiofrequency
receiver coil

## Slide 9: Magnets in the scanner
Layers of magnetic coils in the scanner
  Static magnetic field coil (B0) – lines up proton spins
  Shimming coils – make static magnetic field homogeneous
  Radiofrequency coils – transmit (i.e. sends the B1 field) and receive MR signal
  X, Y, Z gradient coils – localise signal in 3D
2010

## Slide 10: Sequence of events in an MRI scan
2010
Static coil is on all the time
Shimming coil comes on before the start of scanning and maintains constant settings
throughout scanning
RF transmitter coil goes on and off during scanning
RF receiver coil collects MR signal with location
information when the RF transmitter coil is off
X, Y and Z gradient coils come on in various sequences and combinations
(details not shown here) after the RF transmitter coil is switched off and
they help to localise the MR signal in 3D

## Slide 11: Static magnetic field
Very powerful – 1.5 Tesla or more
  Earth’s magnetic field = 0.000031 T
  Small fridge magnet = 0.005 T
  Magnet in a car scrapyard = 1 T
2010

## Slide 12: Static magnetic field
2010

## Slide 13: Static magnetic field
On all the time
Creates a strong (ideally) homogenous magnetic field
Lines up proton spins, which is needed for other coils to work properly
2010

## Slide 14: Shimming coil
MR needs a homogenous magnetic field
Magnetic fields often not homogenous, especially with a human inside them
Can cause artefacts in scan such as image distortions and drop outs
Shimming coil improves this
Shimming is done before the scan and the optimal settings are kept throughout the scan
2010
sinuses
ear
canals

## Slide 15: Radiofrequency (RF) coils
RF coils are used to excite/flip the spins (transmit) and measure signal (receive)
Transmit and receive can be done using the same or different coils.
One coil is located inside the bore (generally used for transmission) and one is located around the subject’s head (normally used to receive signal)
2010
RF transmitter coil
RF receiver coil

## Slide 16: RF transmitter coil
At rest, the axis of the proton’s spin is aligned along B0.
Switching on the RF transmitter coil flips the proton’s spin (flipping of the magnetization).
If it’s a short burst of excitation from the RF transmitter coil, the axis of the proton’s spin precesses about the RF field B1
When the axis of the proton’s spin is flipped by 90o, it ends up in the horizontal plane (typical excitation).
With a longer burst of excitation from the RF transmitter coil, the axis of the proton’s spin points down (180o pulse, or inversion)
2010
Proton spinning
(at rest)
Direction of
magnetic field (B0)
from the static coil
Direction of magnetic
field (B1) from the RF transmitter coil
(RF transmitter
coil is off)
Proton’s axis of spin flipped by 90°
Proton’s axis
of spin flipped
by 180°

## Slide 17: RF receiver coil
After protons have been flipped, the RF transmitter coil is turned off
Flipped protons gradually return to their ‘at rest’ spins
Take different amounts of time, depending on the tissue type
RF receiver coil detects this
This is the basis of the MR signal
Proton spinning
(at rest)
Direction of
magnetic field (B0)
from the static coil
(RF transmitter
coil is switched off)
Proton’s axis of spin
starts to realign with B0
Proton’s axis of spin flipped by 180°
2010

## Slide 18: X, Y, Z gradient coils
X, Y, Z gradient coils locate the MR signal in 3 dimensional space
Make the banging noise during scans
2010
RF receiver coil detects the MR signal but location information also needed

## Slide 19: X, Y, Z gradient coils
Precession frequency is determined by field strength
The field strength can be changed along a gradient in any direction
This creates systematic differences in precession frequency along the directions of the magnetic field gradients
The frequency response from the spins determines their location
Gradient directions:
  X is horizontal (e.g. left to right)
  Y is vertical
  Z is horizontal (e.g. head to toe)
2010

## Slide 20: X, Y, Z gradient coils
Change the strength of the magnetic field along a gradient in different directions
2010
X gradient coil
increases magnetic field
with a gradient of up to 40 mT/m from left to right (in this example)
Z gradient coil
increases magnetic field
with a gradient of
up to 40 mT/m from head to toe
(in this example)
Y gradient coil
increases magnetic field with a gradient
of up to 40 mT/m from bottom to top
(in this example)

## Slide 21: Image formation
MR signals received by the RF coil are processed
Variations in MR signal come from how long it takes proton spins to flip back (relaxation) and whether they have flipped back completely before the next RF transmission pulse
Slices along z-axis
2010

## Slide 22: Image formation
Following excitation, gradient pulses are issued in various sequences and the MR signal is measured
Depending on the sequence in which the gradients are played out, different trajectories can be achieved in each 2D slice:
2010
Straight lines =
echoplanar imaging
Spiral imaging

## Slide 23: Image formation
Results in images of frequencies called k-space
2010
Picture of the Mona Lisa in k-space
Picture of the Mona Lisa in real space

## Slide 24: Image formation
The signal is acquired in k-space. An image in real space is obtained using Fourier transforms
2010
Inverse Fourier
transform
Image of a brain in k-space
The same brain image in real space

## Slide 25: Contrasts
The dynamics of the signal after excitation (T1, T2 relaxations) depend on the tissue properties
White and grey matter have different T1 and T2 relaxation times. As a result, the amount of signal from each tissue type can be tuned, leading to image contrast
The number of protons in each voxel (i.e. proton density) also affects the image contrast
2010

## Slide 26: Contrasts
Types of contrast
  T1 – used for static, detailed images of brain
  T2 – used for static, detailed images of brain
  T2* – used for BOLD
Repetition time (TR), echo time (TE) and excitation flip angle all have an effect on image contrast.
2010

## Slide 27: T1 and T2 contrasts

## Slide 28: T1 contrast
Good for anatomically detailed static images of brain
  White matter lightest
  Grey matter intermediate
  Liquid, e.g. CSF, darkest
2010

## Slide 29: T1 contrast
Slower than T2. At 1.5T:
  Grey matter 900ms
  White matter 600ms
  CSF 4000ms
Intermediate repetition time (TR)
Short echo time (TE) to avoid picking up T2 contrast
More sensitive to artefacts than T2 (T1 uses gradient-echo imaging)
2010
This subject was wearing a hair band with a ~2 mm copper clamp. Left: with hair band. Right: without.
Source: Jorge Jovicich

## Slide 30: T2 contrast
Like a photographic negative of T1
  White matter darkest
  Grey matter intermediate
  Liquid, e.g. CSF, lightest
Used to image tumours and other pathologies
Related to T2* which is important for BOLD
2010

## Slide 31: T2 contrast
Faster than T1. At 1.5T:
  Grey matter 100ms
  White matter 80ms
  CSF 2000ms
Intermediate echo time (TE)
Long repetition time (TR) to avoid picking up T1 signal
Less sensitive to artefacts than T1 (T2 uses spin-echo imaging)
2010

## Slide 32: T2* contrast
Similar to T2
Liquid is brightest
Uses gradient-echo imaging
More sensitive to artefacts than T2
Boring artefacts
  Sinuses, ear canals
Interesting artefacts, aka data
  Blood flow
2010
sinuses
ear
canals
T2* image
T2* image superimposed
on a T1 image

## Slide 33: Recipe for MRI
1) Put subject in big magnetic field (leave him there)
2) Transmit a magnetic field at a 90° angle into subject [about 3 ms]
3) Turn off 90° magnetic field
4) Receive MR signal re-transmitted by subject
  Manipulate re-transmission with gradients of magnetic fields during this readout interval [10-100 ms]
5) Store measured MR signal data vs. time
  Now go back to 2) to get some more data
6) Process raw data to reconstruct images
7) Allow subject to leave scanner (this is optional)
2010

## Slide 34: Hold that thought ...
Main points for understanding BOLD signal
  MRI scanners can distinguish between tissue types
    e.g. white matter, grey matter, liquid
  T2* contrast is used for measuring BOLD signal
2010

## Slide 35: Acknowledgments and references
Antoine for teaching me as much physics as anyone possibly could have
Yen for helping me to get rid of the worst mistakes in my first draft
Previous presenters on Methods for Dummies
Professor Jody Culham of University of Western Ontario for really useful slides and pictures (and to Lea Ernst for the link) http://psychology.uwo.ca/fmri4newbies/Tutorials.html
Huettel SA, Song WA, McCarthy G (2009) Functional Magnetic Resonance Imaging (2nd ed.). Sunderland (Mass.), USA: Sinauer Assoc.
2010

## Slide 36: Another summary that might be useful
2010
Tissue protons align
with magnetic field
(equilibrium state)
RF pulses
Protons absorb
RF energy
(excited state)
Relaxation
processes
Protons emit RF energy
(return to equilibrium state)
Spatial encoding
using magnetic
field gradients
Relaxation
processes
MR signal
detection
Repeat
K-space
Fourier transform
IMAGE
Magnetic field

## Slide 37: What happens to protons in an MRI scan (the real explanation)
When protons are at rest, MR signal cannot be detected. In order to detect an MR signal, you first need RF excitation
RF excitation/flipping the magnetization
  RF excitation is used to flip the magnetization perpendicular to B0.
  When the RF is switched off, protons precess about the B0 field and signal can be detected
  Energy emitted by the protons when they precess
Spin precession
  Following excitation, precession of the spins is determined by the strength of the magnetic field
  Applying gradients of magnetic field changes the local spin precession frequency and is used to determine spin’s locations
A typical sequence consists of: excitation-apply gradients-measure signal
2010