## Slide 1: 1st level analysis: basis functions and correlated regressors
Methods for Dummies 03/12/2014
Steffen Volz
Faith Chiu

## Slide 2: Overview
Part 1: basis functions (Steffen Volz)
Modeling of the BOLD signal
What are basis functions
Which choice of basis functions
Part 2: correlated regressors (Faith Chiu)
…

## Slide 3: Where are we?
Normalisation
Statistical Parametric Map
Image time-series
Parameter estimates
General Linear Model
Realignment
Smoothing
Design matrix
Anatomical reference
Spatial filter
Statistical Inference
RFT
p <0.05

## Slide 4: Modeling of the BOLD signal
BOLD signal is not a direct measure of neuronal activity, but a function of the blood oxygenation, flow and volume (Buxton et al, 1998)  hemodynamic response function (HRF)
The response is delayed compared to stimulus
The response extends over about 20s  overlap with other stimuli
Response looks different between regions (Schacter et al 1997) and subjects (Aguirre et al, 1998)
 Model signal within General Linear Model (GLM)

## Slide 5: Modeling of the BOLD signal
Properties of BOLD response:
Initial undershoot (Malonek & Grinvald, 1996)
Peak after about 4-6s
Final undershoot
Back to baseline after 20-30s
Brief
Stimulus
Undershoot
Initial
Undershoot
Peak

## Slide 6: Temporal basis functions
BOLD response can look different between ROIs and subjects
To account for this temporal basis functions are used for modeling within General Linear Model (GLM)
every time course can be constructed by a set of basis functions
D

## Slide 7: Temporal basis functions
BOLD response can look different between ROIs and subjects
To account for this temporal basis functions are used for modeling within General Linear Model (GLM)
every time course can be constructed by a set of basis functions
Different basis functions:
Fourier basis
Finite impulse response
Gamma functions
Informed basis set

## Slide 8: Temporal basis functions
Finite Impulse Response (FIR):
poststimulus timebins (“mini-boxcars”)
Captures any shape (bin width)
Inference via F-test

## Slide 9: Temporal basis functions
Finite Impulse Response (FIR):
poststimulus timebins (“mini-boxcars”)
Captures any shape (bin width)
Inference via F-test
Fourier Base:
Windowed sines & cosines
Captures any shape (frequency limit)
Inference via F-test

## Slide 10: Temporal basis functions
Gamma Functions:
Bounded, asymmetrical (like BOLD)
Set of different lags
Inference via F-test

## Slide 11: Informed Basis Set (Friston et al. 1998)
Canonical HRF: combination of 2 Gamma functions (best guess of BOLD response)

## Slide 12: Informed Basis Set (Friston et al. 1998)
Canonical HRF: combination of 2 Gamma functions (best guess of BOLD response)
Variability captured by Taylor expansion:
Temporal derivative (account for differences in the latency of response)

## Slide 13: Informed Basis Set (Friston et al. 1998)
Canonical HRF: combination of 2 Gamma functions (best guess of BOLD response)
Variability captured by Taylor expansion:
Temporal derivative (account for differences in the latency of response)
Dispersion derivative (account for differences in the duration of response)

## Slide 14: Basis functions in SPM

## Slide 15: Basis functions in SPM

## Slide 16: Which basis to choose?
Example: rapid motor response to faces (Henson et al, 2001)
canonical HRF alone insufficient to capture full range of BOLD responses
significant additional variability captured by including partial derivatives
combination appears sufficient (little additional variability captured by FIR set)
More complex with protracted processes (eg. stimulus-delay-response) could not be captured
by canonical set, but benefit from FIR set
+ FIR
+ Dispersion
+ Temporal
Canonical

## Slide 17: Summary part 1
Basis functions are used in SPM to model the hemodynamic response either using a single basis function or a set of functions.
The most common choice is the “Canonical HRF” (Default in SPM)
time and dispersion derivatives additionally account for variability of signal change over voxels

## Slide 18: Correlated Regressors
Faith Chiu

## Slide 19: >1 x-value
Linear regression
  y = X.b + e
  Only 1 x-variable
Multiple regression
  Y = β1X1 + β2X2 + … + βLXL + ε
  >1 x-variable

## Slide 20: Multiple regression
y = b0 + b1.x1 + b2.x2
^

## Slide 21: Why are you telling me about this?
In the General Linear Model (GLM) of SPM,
Coefficients (b/β) are parameters which weight the value of your…
Regressors (x1, x2), the design matrix
GLM deals with the time series in voxel in a linear combination
Y = X . β + ε
Observed data
Design matrix
Parameters
Error/residual

## Slide 22: >1 y-value
Linear regression
  y = X.b + e
Single dependent variable y
y = scalar
General linear model (GLM)
  Y = X . β + ε
Multiple y variables: time series in voxel
Y = vector

## Slide 23
BOLD signal
Time
=
1
2
+
+
error
x1
x2
e
Single voxel regression model

## Slide 24
=
+
y
X
Model is specified by both
Design matrix X
Assumptions about e
The design matrix embodies all available knowledge about experimentally controlled factors and potential confounds.
N: number of scans
p: number of regressors
Mass-univariate analysis: voxel-wise GLM

## Slide 25
=
+
Ordinary least squares estimation (OLS) (assuming i.i.d. error):
Objective:
estimate parameters to minimize
y
X
Parameter estimation

## Slide 26
y
e
Design space defined by X
x1
x2
Smallest errors (shortest error vector)
when e is orthogonal to X
Ordinary Least Squares (OLS)
A geometric perspective on the GLM

## Slide 27
x1
x2
x2*
y
When x2 is orthogonalized w.r.t. x1, only the parameter estimate for x1 changes, not that for x2!
Correlated regressors =
explained variance is shared between regressors
Orthogonalisation

## Slide 28: Practicalities re: multicollinearity
Interpreting results of multiple regression can be difficult:
the overall p-value of a fitted model is very low
  i.e. the model fits the data well
but individual p values for the regressors are high
  i.e. none of the X variables has a significant impact on predicting Y
How is this possible?
caused when two (or more) regressors are highly correlated: problem known as multicollinearity

## Slide 29: Multicollinearity
Are correlated regressors a problem?
No
When you want to predict Y from X1 & X2, because R2 and p will be correct
Yes
When you want to assess the impact of individual regressors
Because individual p-values can be misleading: a p-value can be high, even though the variable is improtant

## Slide 30: Final word
When you have correlated regressors, it is very rare that orthogonalisation will be a solution.
  You usually don't have an a priori hypothesis about which regressor should be given the shared variance.
The solution is rather at the stage of the experiment definition where you would make sure by experimental design to decorrelate as much as possible the regressors that you want to look at independently.

## Slide 31: Thanks
Guillaume
SPM course video on GLM
Slides from previous years
Rik Henson’s MRC CBU page:
http://imaging.mrc-cbu.cam.ac.uk/imaging/SpmMiniCourse?action=AttachFile&do=view&target=SPM-Henson-3-design.ppt
http://imaging.mrc-cbu.cam.ac.uk/imaging/DesignEfficiency#Correlation_between_regressors