## Slide 1: M/EEG: Statistical analysis and source localisation
Expert: Vladimir Litvak Mathilde De Kerangal
& Anne Löffler
Methods for Dummies, March 2, 2016

## Slide 2: Statistical analysis in M/EEG
Is signal at a given electrode/sensor related to a specific task?
Where in the brain is this signal generated?
inverse problem
forward problem
sensor-level analysis
source-level analysis

## Slide 3: 1) Sensor-level analysis
Is signal at a given electrode/sensor related to a specific task?
1) Time domain:
Event-related potentials/fields
3) Time & Frequency domain:
Event-related de-/synchronization
2) Frequency domain:
Power spectrum

## Slide 4: 1) Event-related potentials (ERPs)
in MEG: event-related magnetic fields (ERFs)
ERP components in EEG:
  Positive/negative deflections of a certain amplitude
  Measured at a certain latency and recording site
Number of possible t-tests increases with number of
electrodes/sensors
experimental conditions
chosen time windows
α inflation!

## Slide 5: How to avoid α inflation I
a priori specification
  For well-characterized ERP components (e.g., P3)
  Average data over pre-specified sensors and time bins of interest
  One summary statistic per subject per condition
  Comparison with single t-Test/ANOVA
(Silvoni et al., 2009)
What if location of responses is not known a priori, or cannot be localised independently?

## Slide 6: How to avoid α-error inflation II
Topological inference
  Implemented in SPM
  Based on Random Field Theory
  Controls family-wise error rate taking into account neighbouring sensors are not independent
Advantages of RFT in ERP/ERF analyses:
  If data smooth, more sensitive than Bonferroni correction
  No a priori knowledge about time or location of effect required
  No need to average signal over time window
  Requires single summary statistic image

## Slide 7: Summary statistic images
Stack scalp maps over peristimulus time
3D image for each condition: space x space x time
(Litvak et al., 2011)
time
x
y
Epoched data, averaged across trials for each sensor
Generate interpolated scalp map for each time frame

## Slide 8: In SPM
1 data file for each subject and condition
After that: procedure identical to 2nd-level fMRI analysis

## Slide 9: Smoothing
9
Prior to 2nd-level/group analysis
Important to accommodate spatial/temporal variability over subjects and ensure images conform to RFT assumptions
After smoothing: statistical analysis identical to 2nd-level fMRI
Multi-dimensional convolution with Gaussian kernel

## Slide 10: Statistical inference
Compare summary statistic images across conditions
Identify locations in space and time in which a reliable difference occurs
(Litvak et al., 2011)

## Slide 11: 2) Frequency analysis
Neural oscillations
Transform signal from the time domain into the frequency domain
Fourier transform: any signal can be expressed as a combination of different sine waves, each with its own frequency, amplitude and phase

## Slide 12: Power spectrum
Which frequencies contain the signal’s power (energy per unit time)?
E.g., stages of sleep:
(Smietanowski et al., 2006)

## Slide 13: Short-time Fourier transform (STFT)
Discrete Fourier transform requires stationary signal
  No temporal information
STFT allows for analysis of very short time windows
  Uses a sliding window in time  calculates Fourier transform of these snippets of time
Time-Frequency analysis

## Slide 14: 3) Time-frequency analysis
Oscillations in a specific frequency band at a specific time
E.g., event-related synchronization (ERS) and desynchronization (ERD)
(Kilner & Friston, 2010)

## Slide 15: Time-frequency analyses in SPM
Problem: time-frequency data = 4D (time x frequency x space x space)
Topological inference possible for multiple dimensions, but in SPM max. 3D
Dimension reduction required to create single summary statistic image
  If location known a prior: time-frequency maps for a single channel (2D)
  If frequency band known a priori: average across frequency band
    How does power change over space and time (3D)?
15-30 Hz
(Kilner & Friston, 2010)
time
x
y

## Slide 16: Source localisation
Is signal at a given electrode/sensor related to a specific task?
Where in the brain is this signal generated?
inverse problem
forward problem
sensor-level analysis
source-level analysis

## Slide 17
Data
Parameters
Model
Notes: Y our Data,
We have a particular model m which has some parameters theta such as the location or orientation of current sources in the brain.

## Slide 18
Forward Problem
Data
Parameters
Model
Notes: Forward pb defines the likelihood term, probability of the data given the parameters in a particular model, and priors that our model imposes on parameters

## Slide 19
Forward Problem
Inverse Problem
Data
Parameters
Model
Notes: inverse pb. Probability of the parameters given the data in a particular model and the model evidence In order to compare diffeent models

## Slide 20
Forward Problem : Formulation
data
forward
operator
Orientation
Location
Sources parameters

## Slide 21
Forward Problem : Formulation
depends on : - location (orientation) of sensors - geometry of the head - conductivity of the head (source space)
Can have analytic or numeric form.
data
forward
operator
Orientation
Location
Sources parameters

## Slide 22
Source model - current dipole
Current dipole
A
B
I
Q= I * AB AB infinitesimal  Point dipole

## Slide 23
Source model - current dipole
Kirkoff’s law:
Electrical potential
(EEG)
(MEG)
Place a dipole
Simulate quasi-static Maxwell’s Equations
Compute
Compute
Current dipole

## Slide 24
Forward Problem : ECD - Distributed
For large number of (Distributed) dipoles with fixed orientation and location:
is linear in
data
forward
operator
Orientation
Location
Sources parameters
For small number of Equivalent Current Dipoles (ECD) with free location and orientation:
is linear in but non-linear in

## Slide 25
Equivalent current dipole : dipole fit
Select an initial guess for dipole location(s)
2. Calculate the smallest least-squares error between the measurement and the model data achievable by adjusting the dipole orientation(s) and amplitude(s) at this (/those) location(s).
3. If error is the same as in previous iteration step, STOP
4. Find a better candidate for the dipole location(s)
5. Go back to step 2
--> Very robust for one dipole

## Slide 26
Equivalent current dipole : dipole fit Some problems…
A priori fixed number of sources considered.
Contraints on the dipole are difficult to include in the framework and noise cannot properly be taken into account.
Models with different ECDs cannot be compaired, except from goodness of fit which can be miseading, as adding dipoles to a model will necessariy improve the overall goodness of fit.

## Slide 27
Inverse Problem
Data
Parameters
Model
Inverse Problem
Notes: inverse pb. Probability of the parameters given the data in a particular model and the model evidence In order to compare diffeent models

## Slide 28
Inverse Problem

## Slide 29
Inverse Problem

## Slide 30
Inverse Problem
Inverse problem is ill posed. - Many different current distributions can explain the data.
- Solution may be sensitive to noise, i.e., unstable.
Introduction of prior knowledge is needed.
A well-posed problem:
1. A solution exists.
2. The solution depends continuously on the data.
3. The solution is unique.

## Slide 31
Likelihood Prior
Posterior Evidence
Forward Problem
Inverse Problem
Data
Parameters
Model
Bayesian Perspective
Notes: inverse pb. Probability of the parameters given the data in a particular model and the model evidence In order to compare diffeent models

## Slide 32
Variational bayesian Dipole estimation
Standard ECD approaches iterate location/orientation (within a brain volume) until fit to sensor data is maximised (i.e, error minimised). But:
  Local Minima (particularly when multiple dipoles)
  Question of how many dipoles?
With a Variational Bayesian framework, priors can be put on the locations and orientations (and strengths) of dipoles.

## Slide 33
Variational bayesian Dipole estimation
Maximising the (free-energy approximation to the) model evidence offers an answer to question of the number of dipoles.
Likelihood Prior
Posterior
Evidence

## Slide 34
Bayesian Inference : hierarchical linear model
Y = Data n sensors
J = Sources p>>n sources
L = Leadfields n sensors x p sources
E = Error n sensors…
…draw from Gaussian covariance C(e)
Given p sources fixed in location
Data
Lead fields
Error
Sources
Error
Sources
Gaussian Covariance
Gaussian Covariance
Sensor/Source Covariance
Hyper-parameters
Covariance components

## Slide 35
Multiple Sparse Priors
(MSP)
…
# source
# source
Minimum Norm
(IID)
Maximum Smoothness
(LORETA)
Specifying (co)variance components (priors/regularisation)
C = Sensor/Source covariance
Q = Covariance components (known)
λ = Hyper-parameters (unknown)

## Slide 36
Bayesian Inference : iterative estimation scheme
M-step estimate while keeping constants
E-step estimate while keeping constants
Expectation-Maximization (EM) algorithm

## Slide 37
M-step estimate while keeping constants
E-step estimate while keeping constants
Expectation-Maximization (EM) algorithm
Bayesian Inference : iterative estimation scheme
model Mi
Fi
1
2
3
At convergence

## Slide 38
Dynamic Causal Modelling (DCM) can be seen as a source localisation (inverse) method that includes temporal constraints on the source activities. But this will be for another session…
Inverse Problem DCM

## Slide 39: Thank you for your attention! And a big thank you to our expert Vladimir Litvak!

## Slide 40: References
Kilner, J. M., & Friston, K. J. (2010). Topological inference for EEG and MEG. The Annals of Applied Statistics, 1272-1290.
Litvak, V., Mattout, J., Kiebel, S., Phillips, C., Henson, R., Kilner, J., ... & Penny, W. (2011). EEG and MEG data analysis in SPM8. Computational intelligence and neuroscience, 2011.
MfD presentations from previous years
http://imaging.mrc-cbu.cam.ac.uk/meg/IntroEEGMEG#generalanalysis
http://www.timely-cost.eu/sites/default/files/ppts/2ndTrSc/Niko%20Busch%20-%20Time%20frequency%20analysis%20of%20EEG%20data.pdf
http://www.fil.ion.ucl.ac.uk/spm/course/ --> Presentation of Rick Henson
SPM Course : Slides of Jeremie Mattout and Christophe Philip Oct 2008