## Slide 1: Preprocessing: Coregistration and Spatial Normalisation
Cassy Fiford and Demis Kia
Methods for Dummies 2014
With thanks to Gabriel Ziegler

## Slide 2: 1. Preprocessing Recap 2. Coregistration 3. Spatial Normalisation 4. Smoothing 5. SPM help

## Slide 3: Preprocessing Recap: Realignment
Motion Correction
Within subjects
Aligning to a template
fct
fct
fMRI
fct
fct
fct
fMRI

## Slide 4: Preprocessing Recap: Unwarping
Adjusts for changes in field strength
Non linear

## Slide 5: Preprocessing Final Steps: Coregistration
Matching modalities in individual subjects
Normalisation
Matching images to a template (e.g. MNI) across subjects
Smoothing
Adjusts for residual differences and alignment errors
fct
strMRI
fMRI
MNI
fMRI

## Slide 6: Preprocessing Final Steps: Coregistration
Matching modalities in individual subjects
Normalisation
Matching images to a template (e.g. MNI) across subjects
Smoothing
Adjusts for residual differences and alignment errors
fct
strMRI
fMRI
MNI
fMRI

## Slide 7: Coregistration
Intermodal
  Link anatomical information of functional images (few seconds) with a structural image (few minutes)
Intrasubject
Why?
  Superior anatomical localisation
  More precise spatial normalisation
Mean functional
Image
(source)
Anatomical
Image
(reference)
Coregister

## Slide 8: Coregistration
Cannot rely on simply using intensity difference
Identifying individual landmarks too labour intensive

## Slide 9
Seek to measure shared information
  Quantify how well one image predicts the other
Two-step process
  Registration (Fitting source image with reference image)
  Interpolation
    Estimates the intensity of surrounding voxels in functional image  correspond with structural voxels

## Slide 10
    Registration
      Fitting source image (functional) with reference image (structural)

## Slide 11
  Interpolation
    Estimates the intensity of surrounding voxels in functional image  correspond with structural voxels

## Slide 12: Interpolation
Methods include:
Nearest neighbour
Linear interpolation
B-spline interpolation (higher order)
  Same as nearest neighbour and linear in degrees of 0 and 1

## Slide 13: Plotting intensities

## Slide 15: Forming a joint histogram

## Slide 16: Forming a joint histogram

## Slide 17
Registered joint histogram
Misregistered joint histogram

## Slide 18: Normalisation: Motivation
Motivation: A shared space is required to enable us to compare subjects.
Aim: Voxel to voxel correspondence between the brains of subjects

## Slide 19: Why normalise?

## Slide 20: Why normalise cont…
Increases statistical power
Group analysis
Generalisability
Allows cross study comparisons

## Slide 21: Normalisation Native Space  Standard Space
Talairach
Montreal Neurological Insitute (MNI) Space
SPM uses MNI space!

## Slide 22
Normalisation: Procedure
Affine registration 12 dof
  Translations across axes (3 dof)
  Rotations around axes (3 dof)
  Scaling or Zooming (3 dof)
  Shearing or Skewing (3 dof)
A good start…

## Slide 23: Normalisation- Warping
Applies non linear deformations/ displacements from original location to template location
Very Flexible
1000s of dof
Affine Registration
Non-linear Registration

## Slide 24: Normalisation- Overfitting
Flexibility of warping can lead to unrealistic results
Regularisation applies constraints
Non-linear registration
using regularisation.
Non-linear registration
without regularisation.

## Slide 25: Normalisation- Compromise
We need to look at measures of similarity:
Mean squared difference
Squared difference between parameter and expected outcome
The ‘best’ parameters may be unrealistic
Important to use regularisation, to ensure a realistic outcome is found.

## Slide 26: Unified Segmentation
MRI imperfections increase the difficulty of normalisation.
Noise artefacts
Intensity inhomogeneity, bias field
Differences in sequences
Partial Volume

## Slide 27: Unified Segmentation- TPMs
Segmenting subject images before normalising facilitates the normalisation process
Tissue Probability Maps- Standard space structural estimates of the location of GM and WM.
Based on multiple previous segmentations

## Slide 28
+
Tissue Probability Maps
Gaussian Mixture Models
Take each voxel and look at both it’s intensity and prior spatial knowledge, to make normalisation an easier problem to solve.

## Slide 29: Unified Segmentation
Normalising segmented tissue maps to a template a much easier issue to solve than just matching image to template
Helps resolve MRI issues
Bias correction included to combat intensity inhomogeneity

## Slide 30: Smoothing
  Blurs over residual anatomical differences and registration errors
  Why?
  Suppresses noise
    signal reinforced and noise averaged out
  Superior special overlap
  Data becomes more normally distributed
  Increases sensitivity to effects of similar scale to kernel
VS

## Slide 31: Smoothing
How?
Weighted averaging of neighbouring voxels
   Each voxel replaced by the weighted average of itself and its neighbours

## Slide 32: Smoothing: disadvantages
Reduction of spatial resolution of the data
Edge Artifacts
Merging
Extinction
Mislocalization of activation peaks

## Slide 33: Keep in mind
Multiple data adjustments are made during fMRI analysis, and these alter the raw data considerably
   Therefore, large sample sizes and appropriate statistical analyses are required for reliable and robust inferences

## Slide 34: Summary
Coregistration links functional data with a structural image
  Intrasubject
Normalisation links images from one subject to standardised space
Intersubject
Smoothing blurs over any residual errors and anatomical differences

## Slide 35: SPM
spm fmri (to open)
Ensure you have the correct version! (SPM 12) newest update October 2014
If in doubt start by pressing ‘Batch’
All these tools can be found under BatchSPMSpatial
Any images you input make sure are in the correct order (e.g. all prefixed by unique subject identifier, as SPM can’t order your data for you)
Save your batch files so you can retrace your steps
Ensure you have good file structure; SPM spews out tons of files….

## Slide 36: SPM
Reference image- (mean functional DEP image) that is assumed to remain stationary while source is moved to match it.
Source- structural MRI
-----------------------------Unless stated use defaults--------------------------

## Slide 37: SPM- Coregistration Output
Very important to check your images- it automatically loads these up for you!

## Slide 38: SPM- Segment 1
Data- use your structural image.
If using multiple inputs (e.g. T1 and PD weighted image) then ensure all are entered in in the same order.
Tissue 1=GM
Tissue 2=WM
Tissue 3=CSF
Save Bias Corrected.
TBC next slide

## Slide 39: SPM- Segment 2
Scroll down
Data- Forward deformation fields needed for MNI normalisation

## Slide 40: SPM
Use these forward deformations during the normalisation process.
Images to write= co-registered functionals

## Slide 41: SPM
Smooth your normalised images
Choose your kernel width here

## Slide 42: References TPM Ged’s Lecture SPM Homepage Mfd Resources 2013

## Slide 43: THANK YOU Gabriel