## Slide 1: Preprocessing: Coregistration and Spatial Normalisation
Hugo Fleming and Holly Morley
Methods for Dummies 2018
With thanks to our expert John Ashburner

## Slide 2
MNI
str
fct
fct
fct
fct
str
MNI
fct
str
2
MNI
3
1
4
Realign & Unwarp
Coregister
Normalise
Smooth
Raw data
(fct)
Raw data
(str)
MNI
fct
fct
fct
4
is a blurry version of
3
Notes: MNI (Montreal Neurological Institute) – created in a 2-step process based off the Talairach atlas. 1. In a large dataset of brains (n=241), manually defined landmarks and then scaled these to the Talairach atlas. 2. Matched another dataset (n=305) of brains to the average of the brains which had been matched to the Tailarch atlas. Averaged this  the MNI305

## Slide 3: Preprocessing Recap: Realignment
fct
fct
fMRI
fct
fct
fct
fMRI
Motion Correction
Within subjects
Aligning to a template

## Slide 4: Preprocessing Recap: Unwarping
Adjusts for changes in field strength
  Distortions of image resulting from differences in tissue magnetic field susceptibility
Non linear transformations

## Slide 5: Preprocessing: Final Steps Coregistration
Matching modalities in individual subjects
  E.g. functional  structural
Normalisation
Matching images to a template (e.g. MNI) across subjects
Smoothing
Adjusts for residual differences and alignment errors
fct
strMRI
fMRI
MNI
fMRI

## Slide 6: Coregistration
Intrasubject
Intermodal
  Link anatomical information of functional images (T2* weighted) with a structural image (T1 weighted)
Why?
  Superior anatomical localisation in structural image as acquired slower
  More precise spatial normalisation
STRUCTURAL – T1
CO-REGISTRATION
FUNCTIONAL – T2*
– note the poor structural definition

## Slide 7: Coregistration – it’s not simple...
Cannot rely on simply using intensity difference
Identifying individual landmarks too labour intensive
Need a measure of similarity…
Notes: EPI dropout

## Slide 8
Seek to measure shared information
  Registration intuitively relies on the concept of aligning images to increase their similarity
Two-step process
  Registration
  Reslicing (optional)
Coregistration – Approach

## Slide 9
    Registration
      Similar to realignment
      Fitting source image to reference image (static)
      Affine transformation
        Estimate parameters
        Apply these transformations
Notes: An affine transformation is an important class of linear 2-D geometric transformations which maps variables into new variables by applying a linear combination of translation, rotation, scaling and/or shearing (all points along a given line remain fixed while other points are shifted parallel to by a distance proportional to their perpendicular distance from) operations.
Fitting structural to function – simplest but sometimes the coregistration doesn't work so well if there are bias artifacts in the anatomical scan
Fitting functional to structural – need to include all the other fMRI images that should be in alignment with the functional image
This option allows the results of the segmentation (used for bias correction etc) to still be used for spatially normalising all the images.

## Slide 10
    Registration
Fitting structural to function – simplest but sometimes the coregistration doesn't work so well if there are bias artifacts in the anatomical scan
Fitting functional to structural – need to include all the other fMRI images that should be in alignment with the functional image in ‘other images’
This option allows the results of the segmentation (used for bias correction etc) to still be used for spatially normalising all the images.

## Slide 11
  Reslicing (optional)
Reoriented (1x1x3 mm voxel size)
Resliced
(to 2 mm cubic)
Notes: Reslicing – images are resliced to match the reference image (after coregistration)

## Slide 12
  Interpolation
    Estimates the intensity of new voxels in source image corresponding to voxels in the reference space
    Based off intensity of surrounding voxels in original source image
Notes: Not advised – run out of disk space

## Slide 13
Advised to use ‘Estimate only’
The algorithm only changes the headers of the images in order to reflect their new orientation/position.
The changed headers are accounted for by the spatial normalisation routines, so if you estimate a deformation from the anatomical scan, then it can be applied to the functional data
!providing the anatomical and functional scans are in rigid alignment!
Notes: If fitting fcuntional

## Slide 14: Measure of similarity
SPM then mathematically measures the similarity of the two images
  Images are too different to use mean squared difference
  So need measures of image similarity which are more flexible
    Use Mutual Information (Information Theory)
    Derived from joint histograms
Notes: Entropy = randomness

## Slide 15: Plotting intensities
T1 (structural) image
T2* (functional) image
T2* (functional) histogram
T1 (structural) histogram
Intensity
# voxels
Intensity
# voxels

## Slide 16: Forming a joint histogram
Brightness = count of paired intensities

## Slide 17
Registered joint histogram
- More sharpness
Mis-registered joint histogram
- Less sharpness

## Slide 18
Motivation: A shared space is required to enable us to compare subjects.
Aim: Voxel to voxel correspondence between the brains of subjects
Normalisation: why?
Notes: The brains of different subjects vary in shape and size. We want to be able to examine homologous regions across subjects.

## Slide 19: Why normalise? cont’d…
Increases statistical power
Group analysis
Generalise to population level
Allows cross-study comparisons

## Slide 20: Normalisation Native Space  Standard Space
Talairach
Montreal Neurological Institute (MNI) Space
SPM uses MNI space!
Notes: Pooling data to compare activation differences : enables BETWEEN SUBJECTS comparisons to derive group statistics, improve statistical power of analyses, generalise findings to population level, make group analyses: identify similarities and differences between groups; report results in a standard coordinate system
Talairach:
  Not representative of population (single-subject atlas)
  Slices, rather than a 3D volume (from post-mortem slices)
MNI:
  Based on data from many individuals (probabilistic space)
  Fully 3D, data at every voxel  representative average template
  SPM reports MNI coordinates (can be converted to Talairach)
  Shared conventions: AC is roughly [0 0 0], xyz axes = right-left, anterior-post superior-inferior

## Slide 21
Normalisation: Procedure
Affine registration 12 dof
  Translations across axes (3 dof)
  Rotations around axes (3 dof)
  Scaling or Zooming (3 dof)
  Shearing or Skewing (3 dof)
A good start…

## Slide 22
Affine Registration
Non-linear Registration
Normalisation: Procedure
Warping
Applies non linear deformations to move voxels from original location to template location
Very flexible, with 1000s of dof’s

## Slide 23: Warping: how does it work?
In SPM12, warping relies on segmenting the source image into tissue types, using a Gaussian mixture model of signal intensities.

## Slide 24: Warping: how does it work?
Having identified the features of the image (grey matter, white matter etc.), alignment with the standard Tissue Probability Maps is easier.
+

## Slide 25: Non-linear basis functions
Deformations are modelled with a linear combination of non-linear basis functions
Warping in more detail

## Slide 26: Pitfalls of normalisation: overfitting
Flexibility of warping can lead to unrealistic results
Regularisation applies constraints
Non-linear registration
using regularisation.
Non-linear registration
without regularisation.

## Slide 27: Pitfalls of normalisation: overfitting
Regularisation uses priors and constraints to reduce the possibility of overfitting.
Find the best parameters to match the source image to the template whilst simultaneously minimising the deviation of the parameters from expected values.

## Slide 28: Smoothing
  Blurs over residual anatomical differences and registration errors
  Why?
  Suppresses noise
    signal reinforced and noise averaged out
  Superior special overlap
  Data becomes more normally distributed
  Increases sensitivity to effects of similar scale to kernel
VS

## Slide 29: Smoothing
How?
Weighted averaging of neighbouring voxels
   Each voxel replaced by the weighted average of itself and its neighbours

## Slide 30: Smoothing: disadvantages
Reduction of spatial resolution of the data
Edge Artifacts
Merging
Extinction
Mislocalisation of activation peaks

## Slide 31: Keep in mind
Multiple data adjustments are made during fMRI analysis, and these alter the raw data considerably
   Therefore, large sample sizes and appropriate statistical analyses are required for reliable and robust inferences

## Slide 32: Summary
Coregistration links functional data with a structural image
  Intrasubject
Normalisation links images from one subject to standardised space
Intersubject
Smoothing blurs over any residual errors and anatomical differences

## Slide 33: SPM
spm fmri (to open)
Ensure you have the correct version! (SPM 12) newest update October 2014
If in doubt start by pressing ‘Batch’
All these tools can be found under BatchSPMSpatial
Any images you input make sure are in the correct order (e.g. all prefixed by unique subject identifier, as SPM can’t order your data for you)
Save your batch files so you can retrace your steps
Ensure you have good file structure; SPM spews out tons of files….

## Slide 34: SPM
Reference image- (mean functional DEP image) that is assumed to remain stationary while source is moved to match it.
Source- structural MRI
-----------------------------Unless stated use defaults--------------------------

## Slide 35: SPM- Coregistration Output
Very important to check your images- it automatically loads these up for you!

## Slide 36: SPM- Segment 1
Data- use your structural image.
If using multiple inputs (e.g. T1 and PD weighted image) then ensure all are entered in in the same order.
Tissue 1=GM
Tissue 2=WM
Tissue 3=CSF
Save Bias Corrected.
TBC next slide
Notes: A bias field is a smooth low frequency signal that corrupts MRI images due to inhomogeneities in the magnetic fields of MRI machine

## Slide 37: SPM- Segment 2
Scroll down
Data- Forward deformation fields needed for MNI normalisation

## Slide 38: SPM
Use these forward deformations during the normalisation process.
Images to write= co-registered functionals

## Slide 39: SPM
Smooth your normalised images
Choose your kernel width here

## Slide 40: References John’s Lecture Ged Ridgway’s preprocessing lecture SPM Homepage Mfd Resources 2018