## Slide 1: Basis of M/EEG signals (Part 1)
Yue Kong
Muhammad Akil Yerilwan Putra
March 23, 2022

## Slide 2: Overview
Introduction to EEG
Basis of EEG signals
Basic principles of EEG recording
Extra:
  EEG signatures (ERP and oscillations)
  Frequency spectrum (waves)
  Clinical applications

## Slide 3: Introduction to EEG
EEG (Electroencephalogram): a way to measure electrical activity in the brain (cortex)
Characteristics:
  Direct and non-invasive
  Excellent temporal resolution
  Can be mobile
  Combined with other imaging techniques
  Commonly used to detect seizure and epileptic activity
Adapted from
Mehta & Parasuraman, 2013

## Slide 4: Basis of EEG signals
Types of Voltage:
Action potential: discrete voltage spikes that travel from the beginning of the axon at the cell body to the axon terminals, where neurotransmitter are released.
Postsynaptic potentials (PSP): voltages that arise when the neurotransmitters bind to receptors on the membrane of the postsynaptic cell.
EEG reflects summed post synaptic activity of large cell ensembles.
(EPSP)
(IPSP)
https://mathsgee.com/learn/mod/page/view.php?id=10385

## Slide 5: Basis of EEG signals
Dipole: a region of positive charge separated from a region of negative charge by some distance.
The region of positive charge is referred to as a source, while the region of negative charge is referred to as a sink.
Electrodes detect the sum of positive and negative charges in their proximity.
Radial dipole
Tangential dipole
Jackson & Bolger, 2014

## Slide 6: Basis of EEG signals
To produce a measurable (nonzero) signal, neurons must be both arranged in a parallel fashion, and synchronously active.
This is most likely to occur in cortical pyramidal cells, which are aligned perpendicular to the surface of the cortex.
Jackson & Bolger, 2014

## Slide 7: Basis of EEG signals
Either an EPSP near the soma or an IPSP at the apical dendrites.
Measured EEG cannot determine if activity is excitatory or inhibitory.
Jackson & Bolger, 2014
Either an IPSP (which produces an extracellular positivity) near the soma, or an EPSP (which produces an extracellular negativity) at the apical dendrites.

## Slide 8: Spatial resolution
The low spatial resolution is attributable to:
Limited number of sensors
Volume conduction

## Slide 9: Measuring an EEG-signal
The 10 – 20 system : standardised placement
EEG system: electrodes, differential amplifier, recording PC and stimulus PC.
The way the electrodes are connected to the amplifiers are referred to as a montage
Ueda, Sakai and Yanagisawa, (2019)
Modir (2017)
Nasion
Inion
Auricullar points
Auricullar points

## Slide 10: Mobile EEG
Lau-Zhu et al., 2019

## Slide 11
Frequency Spectrum (waves)
(Sakhavi 2017)
>
Notes: For comparison.
There are a lot more waves and specific wave components which appear depending on circumstances.

## Slide 12: Common signatures
Event-related potential (ERP): transient activity, time-locked to an event, most often an external stimulus.
Neural oscillations: frequency specific patterns of neural activity
Spontaneous oscillations (e.g. sensorimotor rhythm, alpha rhythm)
Induced oscillations (e.g. steady-state visual evoked potentials (SSVEP), evoked by an synchronous to a periodic external stimulus)
Wikipedia
Berlin BCI

## Slide 13
Clinical/Experimental Application
EEG monitoring is actively in daily clinical practice.
  Monitoring and treatment patients
Detection of burst suppression on anaesthesia
Detection of cerebral ischemia
Prognostication outcomes
  In cases with significant/permanent damage
  Cognitive function
  Coma
(Sun et al 2020)
Epilepsy
Parkinson’s disease
Memory problems (“Alzheimer’s”)
Seizures
Post traumatic stress disorder
Language impairments (“Dyslexia”)
Sleep disorders and insomnia
(Soufineyestani et al 2020)
Notes: EEG used in practice for its key sensitivity to detect neurophysiological changes in the brain.

## Slide 14: Advantages and Disadvantages
Advantages
Ongoing / real time activity
Non-invasive
Low-cost
Quiet
High temporal resolution
Minimal safety concerns
Disadvantages
Poor spatial resolution
High noise
Subjective
Requires a trained physiologist to run and read the recording

## Slide 15: Jackson, A. F., & Bolger, D. J. (2014). The neurophysiological bases of EEG and EEG measurement: A review for the rest of us. Psychophysiology, 51(11), 1061-1071. Lau- Zhu, A., Lau, M, P,H. & McLoughlin,G. (2019). Mobile EEG in research on neurodevelopmental disorders: Opportunities and challenges. Developmental Cognitive Neuroscience. 36, https://doi.org/10.1016/j.dcn.2019.100635 Mehta, R. K., & Parasuraman, R. (2013). Neuroergonomics: a review of applications to physical and cognitive work. Frontiers in human neuroscience, 7, 889. Modir, A. (2017). NIRS signal evaluation in order to epileptic seizure detection. 10.13140/RG.2.2.23784.32007. Ueda, K., Sakai, Y., & Yanagisawa, H. (2019). Quantitative evaluation of sense of discrepancy to operation response using event-related potential. https://arxiv.org/pdf/1907.01827.pdf Soufineyestani, S., Dowling, D., Khan, A., 2020. Electroencephalography (EEG) Technology Applications and Available Devices. Applied Sciences, University of Minnesota Duluth. https://webcache.googleusercontent.com/search?q=cache:6_gW1h8XfiwJ:https://www.mdpi.com/2076-3417/10/21/7453/pdf+&cd=13&hl=en&ct=clnk&gl=uk&client=safari Sun, Y., Wei, C., Cui, V., Xiu, M., & Wu, A., 2020. Electroencephalography: Clinical Applications During the Perioperative Period. Frontiers in medicine, 7, 251. https://doi.org/10.3389/fmed.2020.00251 https://www.brightbraincentre.co.uk/electroencephalogram-eeg-brainwaves/ https://mathsgee.com/learn/mod/page/view.php?id=10385
References

## Slide 16: Basis of M/EEG signals (Part 2)
Yue Kong
Muhammad Akil Yerilwan Putra
March 23, 2022

## Slide 17: Outline
MEG: magnetoencephalography, measure changes in magnetic flux density outside of the head
Where do MEG signals come from
How do we record them
What do they mean
EEG versus MEG

## Slide 18: Outline
Where do MEG signals come from
How do we record them
What do they mean
EEG versus MEG

## Slide 19: Where do MEG signals come from
Pyramidal cells / stellate cells
  in layer II/III and V
  perpendicular to the surface
  synchronous
EPSP / action potentials
Intracellular / extracellular currents
Sulci / gyri *
gyrus
sulcus
* Generally speaking

## Slide 20: Outline
Where do MEG signals come from
How do we record them
What do they mean
EEG versus MEG

## Slide 21: How do we record them
Magnetically Shielded Room
  earth: 25~65 x 10-6 T; brain: 10-15 T
SQUIDs: Superconducting QUantum Interference Device
  superconducting: 0 resistance  infinite conductivity
  below 4 K (-269.15 °C), using liquid helium
Don’t move!
  3D-printed headcast

## Slide 22: How do we record them

## Slide 23: How do we record them

## Slide 24: How do we record them
OPM (Optically pumped magnetometers)
  Portable
  Shorter distance  higher SNR
OPM (2018)
WCHN (2021)

## Slide 25: Outline
Where do MEG signals come from
How do we record them
What do they mean
EEG versus MEG

## Slide 26: What do they mean
Temporal * spatial * spectral
  Careful! Domain reduction can deceive (Zich, 2020, TiCS)
Epoch
  Trial average (ERF)
  Time-frequency analysis
Source localization
  Orientation
  Extent
  Depth
Forward & Inverse problem
Neuronal activity/
Current density
EEG/MEG Sensor data
Forward modelling:
easy!

## Slide 27: Outline
Where do MEG signals come from
How do we record them
What do they mean
EEG versus MEG

## Slide 28: EEG versus MEG
 | EEG | MEG
Temporal resolusion | ms | ms
Spatial resolusion | poor | good
Source of signals | Deep and shallow dipoles | mainly shallow dipoles
 | Gyri and sulci | Mainly sulci
Quality of signals | Affected by skull, meninges | Unaffected by skull, meninges
SNR* | low | high
feasibility | Cheap, widely available | Expensive, limited availability
* EEG needs 3 times of data to get the same results with MEG (Florian Destoky et al., 2018, Neuroimage)