## Slide 1: fMRI Preprocessing
Guillaume Flandin
Wellcome Trust Centre for Neuroimaging
University College London
SPM Course
Chicago, 22-23 Oct 2015

## Slide 2
Normalisation
Statistical Parametric Map
Image time-series
Parameter estimates
General Linear Model
Realignment
Smoothing
Design matrix
Anatomical reference
Spatial filter
Statistical Inference
RFT
p <0.05

## Slide 3
Realign
fMRI time series
Structural MRI
Template
Smoothed fMRI
Deformation
Smooth
Coregister
Write Normalised
Normalise/Segment






## Slide 4: Contents
Registration basics
Motion and realignment
Inter-modal coregistration
Spatial normalisation
Gaussian smoothing

## Slide 5: Contents
Registration basics
  Voxel-to-world mapping
  Transformation
  Similarity measure
  Optimisation
  Interpolation
Motion and realignment
Inter-modal coregistration
Spatial normalisation
Gaussian smoothing

## Slide 6: Representation of imaging data
Three dimensional images are made up of voxels.
Voxel intensities are stored on disk as lists of numbers.
Meta-information about the data:
  The image dimensions
    Allowing conversion from list to 3D array
  The “voxel-to-world mapping”
    Spatial transformation that maps from data coordinates (voxel column i, row j, slice k) into a real-world position (x,y,z mm) in a coordinate system e.g.:
      Scanner coordinates
      T&T/MNI coordinates

## Slide 7: Image registration
Process of transforming different set of images into one coordinate system.
Two key ingredients:
  Transformation type:
    Rigid
    Affine
    Non-linear
  Similarity measure:
    Mean-squared difference
    Correlation coefficient
    Mutual information
Within-subject
Between-subject
Within-modality
Between-modality

## Slide 8: Optimisation
Automatic image registration is done by using an optimisation algorithm.
Optimisation involves finding some “best” parameters according to an “objective function”, which is either minimised or maximised.
Value of parameter
Objective function
Most probable solution (global optimum)
Local optimum
Local optimum

## Slide 9: Reslicing / Interpolation
Reoriented (1x1x3 mm voxel size)
Resliced
(to 2 mm cubic)
Applying the transformation parameters, and re-sampling the data onto the same grid of voxels as the target image
  reslicing, interpolation, regridding, transformation, and writing

## Slide 10: Simple Interpolation
Nearest neighbour
  Take the value of the closest voxel
Tri-linear
  Just a weighted average of the neighbouring voxels
  f5 = f1 x2 + f2 x1
  f6 = f3 x2 + f4 x1
  f7 = f5 y2 + f6 y1

## Slide 11: B-spline Interpolation
B-splines are piecewise polynomials
A continuous function is represented by a linear combination of basis functions
2D B-spline basis functions of degrees 0, 1, 2 and 3
Nearest neighbour and trilinear interpolation are the same as B-spline interpolation with degrees 0 and 1.

## Slide 12: Contents
Registration basics
Motion and realignment
Inter-modal coregistration
Spatial normalisation
Gaussian smoothing

## Slide 13: Motion correction
Head movement is a very large source of variance in fMRI data.
Motion correction: realign a time-series of images acquired from the same subject.
  Within-subject transformation: rigid-body (6 parameters)
  Within-modality: least squares objective function
0
10
20
30
40
50
60
70
80
90
-0.4
-0.2
0
0.2
0.4
image
mm
translation
x translation
y translation
z translation
0
10
20
30
40
50
60
70
80
90
-0.2
0
0.2
0.4
0.6
image
degrees
rotation
pitch
roll
yaw

## Slide 14: Residual Errors from aligned fMRI
Slices are not acquired simultaneously
  rapid movements not accounted for by rigid body model
Resampling can introduce interpolation errors
  especially tri-linear interpolation
Image artefacts may not move according to a rigid body model
  image distortion
  image dropout
Functions of the estimated motion parameters can be modelled as confounds in subsequent analyses

## Slide 15: Movement by Distortion Interaction of fMRI
Subject disrupts B0 field, rendering it inhomogeneous
  Distortions in phase-encode direction
Subject moves during EPI time series
  Distortions vary with subject orientation
  Shape varies (non-rigidly)
“Realign & Unwarp”: generative model that combines a model of geometric distortions and a model of subject motion to correct images.

## Slide 16
No correction
Correction by covariation
Correction by Unwarp
No correction
Movement correction strategies

## Slide 17: Contents
Registration basics
Motion and realignment
Inter-modal coregistration
Spatial normalisation
Gaussian smoothing

## Slide 18: Coregistration (intra-subject, inter-modal)
Inter-modal registration.
Match images from same subject but different modalities:
anatomical localisation of single subject activations
achieve more precise spatial normalisation of functional image using anatomical image.

## Slide 19: Coregistration maximises Mutual Information
Joint histogram sharpness correlates with image alignment. Mutual information and related measures attempt to quantify how well one image predicts the other.
Between-modality registration: Seek to measure shared information in some sense.

## Slide 20: Coregistration

## Slide 21: Contents
Registration basics
Motion and realignment
Inter-modal coregistration
Spatial normalisation
  Unified segmentation
Gaussian smoothing

## Slide 22: Spatial Normalisation

## Slide 23: Spatial Normalisation - Reasons
Inter-subject averaging
  Increase sensitivity with more subjects
    Fixed-effects analysis
  Extrapolate findings to the population as a whole
    Random-effects analysis
Make results from different studies comparable by aligning them to standard space.

## Slide 24: Standard spaces
The MNI template follows the convention of T&T, but doesn’t match the particular brain (http://imaging.mrc-cbu.cam.ac.uk/imaging/MniTalairach)
Talairach Atlas
MNI/ICBM AVG152 Template

## Slide 25: Unified Segmentation
Normalising segmented tissue maps should be more robust and precise than using the original images.
Tissue segmentation benefits from spatially-aligned prior tissue probability maps.
Combining normalisation and segmentation in a unified model:
  Gaussian mixture model segmentation
  Intensity inhomogeneity (bias field) correction
  Warping (non-linear registration)

## Slide 26: Tissue intensity distributions (T1-weighted MRI)

## Slide 27: Mixture of Gaussians
Classification is based on a Mixture of Gaussians model, which represents the intensity probability density by a number of Gaussian distributions.
Image Intensity
Frequency

## Slide 28: Non-Gaussian Intensity Distributions
Multiple Gaussians per tissue class allow non-Gaussian intensity distributions to be modelled.
  E.g. accounting for partial volume effects

## Slide 29: Modelling inhomogeneity
A multiplicative bias field is modelled as a spatially smooth image (a linear combination of basis functions).
Corrupted image
Corrected image
Bias Field

## Slide 30: Tissue Probability Maps
Each TPM indicates the prior probability for a particular tissue at each point in MNI space.
SPM12’s TPMs are derived from the IXI dataset initialised with the ICBM 452 atlas and other data.

## Slide 31: Deforming the Tissue Probability Maps
Tissue probability images are warped to match the subject.
The inverse transform warps to the TPMs.
Warps are constrained to be reasonable by penalising various distortions (regularisation).

## Slide 32: Spatial Normalisation – Overfitting
Template
image
Affine registration.
(SSE = 472.1)
Non-linear
registration
without
regularisation.
(SSE = 287.3)
Non-linear
registration
using
regularisation.
(SSE = 302.7)
Without regularisation, the non-linear normalisation can introduce unnecessary deformation

## Slide 33: Spatial Normalisation – Results
Non-linear registration
Affine registration

## Slide 34: Spatial Normalisation – Limitations
Seek to match functionally homologous regions, but...
  No exact match between structure and function
  Different cortices can have different folding patterns
  Challenging high-dimensional optimisation, many local optima
Compromise
  Correct relatively large-scale variability (sizes of structures)
  Smooth over finer-scale residual differences

## Slide 35: Contents
Registration basics
Motion and realignment
Inter-modal coregistration
Spatial normalisation
Gaussian smoothing

## Slide 36: Smoothing
Why would we deliberately blur the data?
  Improves spatial overlap by blurring over minor anatomical differences and registration errors
  Averaging neighbouring voxels suppresses noise
  Increases sensitivity to effects of similar scale to kernel (matched filter theorem)
  Makes data more normally distributed (central limit theorem)
  Reduces the effective number of multiple comparisons
How is it implemented?
  Convolution with a 3D Gaussian kernel, of specified full-width at half-maximum (FWHM) in mm
Notes: Spatial normalisation is never exact, so homologous regions can never be precisely registered. Furthermore, due to the noisy nature of the BOLD signal, activations from different scans can be slightly offset, thereby cancelling each other out. Smoothing spreads out the different areas and reduces the discrepancy.

## Slide 37: Effect of smoothing
3D Gaussian smoothing with FWHM: 0, 2, 4, 6, 8, 10, 12, 14, 16 mm isotropic

## Slide 38
Realign
fMRI time series
Structural MRI
Template
Smoothed fMRI
Deformation
Smooth
Coregister
Write Normalised
Normalise/Segment






## Slide 39
Normalise/Segment
Realign
fMRI time series
Structural MRI
Template
Smoothed fMRI
Deformation
Smooth
Coregister
Write Normalised






## Slide 40
Realign
fMRI time series
Template
Smoothed fMRI
Deformation
Smooth
Write Normalised




Normalise/Segment

## Slide 41: References
Friston et al. Spatial registration and normalisation of images. Human Brain Mapping 3:165-189 (1995).
Collignon et al. Automated multi-modality image registration based on information theory. IPMI’95 pp 263-274 (1995).
Thévenaz et al. Interpolation revisited. IEEE Trans. Med. Imaging 19:739-758 (2000).
Andersson et al. Modeling geometric deformations in EPI time series. Neuroimage 13:903-919 (2001).
Ashburner & Friston. Unified Segmentation. NeuroImage 26:839-851 (2005).
Klein et al. Evaluation of 14 nonlinear deformation algorithms applied to human brain MRI registration. NeuroImage 46(3):786-802 (2009).

## Slide 42: Spatial normalisation with DARTEL
Limitation of current approach:
  Limited flexibility (low DoF) registration has been criticised
  Inverse transformations are useful, but not always well-defined
  More flexible registration requires careful modelling and regularisation (prior belief about reasonable warping)
  MNI/ICBM templates/priors are not universally representative
The DARTEL toolbox combines several methodological advances to address these limitations.

## Slide 43
Realign
fMRI time series
Structural MRI
Template
Smoothed fMRI
Deformation
DARTEL Create template
Coregister
DARTEL Norm to MNI
and Smooth





Segment
…

## Slide 44
Evaluations of nonlinear registration algorithms