## Slide 1: Event-related fMRI
Guillaume Flandin
Wellcome Trust Centre for Neuroimaging
University College London
SPM Course
Chicago, 22-23 Oct 2015

## Slide 2: BOLD response
Brief
Stimulus
Undershoot
Peak
Early event-related fMRI studies used a long Stimulus Onset Asynchrony (SOA) to allow BOLD response to return to baseline.
However, overlap between successive responses at short SOAs can be accommodated if the BOLD response is explicitly modeled, particularly if responses are assumed to superpose linearly.
Shape of the BOLD response add constraints on design efficiency.

## Slide 3
Slice Timing issue
t1 = 0 s
t16 = 2 s
T=16, TR=2s
t0 = 8
t0 = 16

## Slide 4
Slice Timing issue
“Slice-timing Problem”:
‣ Slices acquired at different times, yet
model is the same for all slices
‣ different results (using canonical HRF) for different reference slices
‣ (slightly less problematic if middle slice is selected as reference, and with short TRs)
Solutions:
1. Temporal interpolation of data
“Slice timing correction”
2. More general basis set (e.g., with temporal derivatives)
Top slice
Bottom slice
Interpolated
Derivative
See Sladky et al, NeuroImage, 2012.
TR=3s

## Slide 5: Timing issues: Sampling
Scans
TR=4s
Stimulus (synchronous)
SOA=8s
Stimulus (asynchronous)
Stimulus (random jitter)
Typical TR for 48 slice EPI at 3mm spacing is ~ 4s
Sampling at [0,4,8,12…] post- stimulus may miss peak signal.
Higher effective sampling by:
Asynchrony eg SOA=1.5TR
2. Random Jitter eg SOA=(2±0.5)TR

## Slide 6
Optimal SOA?
Not very efficient…
Very inefficient…
16s SOA
4s SOA

## Slide 7: Short randomised SOA
Stimulus (“Neural”)
HRF
Predicted Data
More efficient!

=
Null events

## Slide 8: Block design SOA
Stimulus (“Neural”)
HRF
Predicted Data
Even more efficient!

=

## Slide 9
Design efficiency
HRF can be viewed as a filter.
We want to maximise the signal passed by this filter.
Dominant frequency of canonical HRF is ~0.03 Hz.
The most efficient design is a sinusoidal modulation of neuronal activity with period ~32s

## Slide 10
Sinusoidal modulation, f=1/32
Fourier Transform
Fourier Transform
=
Stimulus (“Neural”)
HRF
Predicted Data

=

=

## Slide 11

=

=
Stimulus (“Neural”)
HRF
Predicted Data
Fourier Transform
Fourier Transform
Blocked: epoch = 20s

## Slide 12

=

=
Predicted Data
HRF
Stimulus (“Neural”)
Fourier Transform
Fourier Transform
Blocked: epoch = 80s, high-pass filter = 1/120s

## Slide 13
Randomised Design, SOAmin = 4s, high pass filter = 1/120s
Fourier Transform
Fourier Transform

=

=
Stimulus (“Neural”)
HRF
Predicted Data
Randomised design spreads power over frequencies

## Slide 14: Design efficiency
The aim is to minimize the standard error of a t-contrast (i.e. the denominator of a t-statistic).
This is equivalent to maximizing the efficiency e:
Noise variance
Design variance
If we assume that the noise variance is independent of the specific design:
This is a relative measure: all we can really say is that one design is more efficient than another (for a given contrast).

## Slide 15: Design efficiency
A
B
A+B
A-B
High correlation between regressors leads to low sensitivity to each regressor alone.
We can still estimate efficiently the difference between them.

## Slide 16: Example: working memory
B: Jittering time between stimuli and response.
Stimulus
Response
Stimulus
Response
Stimulus
Response
A
B
C
Time (s)
Time (s)
Time (s)
Correlation = -.65 Efficiency ([1 0]) = 29
Correlation = +.33 Efficiency ([1 0]) = 40
Correlation = -.24 Efficiency ([1 0]) = 47
C: Requiring a response on a randomly half of trials.

## Slide 17
Happy (A) vs sad (B) faces: need to know both (A-B) and (A + B)
 | A | B
A | 0.5 | 0.5
B | 0.5 | 0.5
Transition matrix
Efficiency Example #1
Two event types, A and B
Randomly intermixed: ABBAABABB…
Optimising the SOA
Differential Effect (A-B)
Common Effect (A+B)
SOA (s)
Efficiency

## Slide 18
Happy (A) vs sad (B) faces: need to know both (A-B) and (A + B)
Optimising the SOA
 | A | B
A | 0.33 | 0.33
B | 0.33 | 0.33
Transition matrix
(A+B)
(A-B)
SOA (s)
Efficiency
Efficiency Example #2
Two event types, A and B
Randomly intermixed with null events: AB-BAA--B---ABB…
Efficient for differential and main effects at short SOA
Equivalent to stochastic SOA

## Slide 19: Design efficiency
Block designs:
Generally efficient but often not appropriate.
Optimal block length 16s with short SOA (beware of high-pass filter).
Event-related designs:
Efficiency depends on the contrast of interest
With short SOAs ‘null events’ (jittered ITI) can optimise efficiency across multiple contrasts.
Non-linear effects start to become problematic at SOA<2s
http://imaging.mrc-cbu.cam.ac.uk/imaging/DesignEfficiency

## Slide 20: Multiple testing (random field theory)
Guillaume Flandin
Wellcome Trust Centre for Neuroimaging
University College London
SPM Course
Chicago, 22-23 Oct 2015

## Slide 21
Pre- processings
General Linear Model
Statistical Inference
Contrast c
Random
Field Theory

## Slide 22: Inference at a single voxel
Null distribution of test statistic T
u
Decision rule (threshold) u: determines false positive rate α
Null Hypothesis H0: zero activation
 Choose u to give acceptable α under H0

## Slide 23: Multiple tests
t

u
t

u
t

u
t

u
t

u
t

u
Signal
If we have 100,000 voxels,
α=0.05  5,000 false positive voxels.
This is clearly undesirable; to correct for this we can define a null hypothesis for a collection of tests.
Noise

## Slide 24: Multiple tests
t

u
t

u
t

u
t

u
t

u
t

u
11.3%
11.3%
12.5%
10.8%
11.5%
10.0%
10.7%
11.2%
10.2%
9.5%
Use of ‘uncorrected’ p-value, α =0.1
Percentage of Null Pixels that are False Positives
If we have 100,000 voxels,
α=0.05  5,000 false positive voxels.
This is clearly undesirable; to correct for this we can define a null hypothesis for a collection of tests.

## Slide 25: Family-Wise Null Hypothesis
FWE
Use of ‘corrected’ p-value, α =0.1
Use of ‘uncorrected’ p-value, α =0.1
Family-Wise Null Hypothesis:
Activation is zero everywhere
If we reject a voxel null hypothesis at any voxel, we reject the family-wise Null hypothesis
A FP anywhere in the image gives a Family Wise Error (FWE)
Family-Wise Error rate (FWER) = ‘corrected’ p-value

## Slide 26: Bonferroni correction
The Family-Wise Error rate (FWER), αFWE, for a family of N tests follows the inequality:
where α is the test-wise error rate.
Therefore, to ensure a particular FWER choose:
This correction does not require the tests to be independent but becomes very stringent if dependence.

## Slide 27: Spatial correlations
100 x 100 independent tests
Spatially correlated tests (FWHM=10)
Bonferroni is too conservative for spatially correlated data.
Discrete data
Spatially extended data

## Slide 28: Topological inference
Topological feature:
Peak height
space
intensity
Peak level inference

## Slide 29: Topological inference
Topological feature:
Cluster extent
space
intensity
uclus
uclus : cluster-forming threshold
Cluster level inference

## Slide 30: Topological inference
Topological feature:
Number of clusters
space
intensity
uclus
uclus : cluster-forming threshold
c
Set level inference

## Slide 31: RFT and Euler Characteristic
Search volume
Roughness (1/smoothness)
Threshold

## Slide 32: Random Field Theory
The statistic image is assumed to be a good lattice representation of an underlying continuous stationary random field. Typically, FWHM > 3 voxels (combination of intrinsic and extrinsic smoothing)
Smoothness of the data is unknown and estimated: very precise estimate by pooling over voxels  stationarity assumptions (esp. relevant for cluster size results).
A priori hypothesis about where an activation should be, reduce search volume  Small Volume Correction:
  mask defined by (probabilistic) anatomical atlases
  mask defined by separate "functional localisers"
  mask defined by orthogonal contrasts
  (spherical) search volume around previously reported coordinates

## Slide 33: Conclusion
There is a multiple testing problem and corrections have to be applied on p-values (for the volume of interest only (see Small Volume Correction)).
Inference is made about topological features (peak height, spatial extent, number of clusters). Use results from the Random Field Theory.
Control of FWER (probability of a false positive anywhere in the image): very specific, not so sensitive.
Control of FDR (expected proportion of false positives amongst those features declared positive (the discoveries)): less specific, more sensitive.

## Slide 34: Statistical Parametric Maps
mm
mm
mm
time
mm
time
frequency
fMRI, VBM, M/EEG source reconstruction
M/EEG 2D time-frequency
M/EEG 2D+t scalp-time
M/EEG 1D channel-time
time
mm

## Slide 35: Group Analyses
SPM Course
Chicago, 22-23 Oct 2015
Guillaume Flandin
Wellcome Trust Centre for Neuroimaging
University College London

## Slide 36
Normalisation
Statistical Parametric Map
Image time-series
Parameter estimates
General Linear Model
Realignment
Smoothing
Design matrix
Anatomical reference
Spatial filter
Statistical Inference
RFT
p <0.05

## Slide 37
GLM: repeat over subjects
fMRI data
Design Matrix
Contrast Images
SPM{t}
Subject 1
Subject 2
…
Subject N

## Slide 38
Fixed effects analysis (FFX)
Subject 1
Subject 2
Subject 3
Subject N
…
Modelling all subjects at once
Simple model
Lots of degrees of freedom
Large amount of data
Assumes common variance over subjects at each voxel

## Slide 39
Fixed effects analysis (FFX)
=
+
Modelling all subjects at once
Simple model
Lots of degrees of freedom
Large amount of data
Assumes common variance over subjects at each voxel

## Slide 40
Probability model underlying random effects analysis
Random effects

## Slide 41
With Fixed Effects Analysis (FFX) we compare the group effect to the within-subject variability. It is not an inference about the population from which the subjects were drawn.
With Random Effects Analysis (RFX) we compare the group effect to the between-subject variability. It is an inference about the population from which the subjects were drawn. If you had a new subject from that population, you could be confident they would also show the effect.
Fixed vs random effects

## Slide 42
Fixed isn’t “wrong”, just usually isn’t of interest.
Summary:
  Fixed effects inference:
  “I can see this effect in this cohort”
  Random effects inference:
  “If I were to sample a new cohort from the same
  population I would get the same result”
Fixed vs random effects

## Slide 43
=
Example: Two level model
+
=
+
Second level
First level
Hierarchical models
Mixed-effects and fMRI studies. Friston et al., NeuroImage, 2005.

## Slide 44
Summary Statistics RFX Approach
Contrast Images
fMRI data
Design Matrix
Subject 1
…
Subject N
First level
  Generalisability, Random Effects & Population Inference. Holmes & Friston, NeuroImage,1998.
Second level
One-sample t-test @ second level
Notes: Two-stage procedure

## Slide 45
Summary Statistics RFX Approach
Assumptions
The summary statistics approach is exact if for each session/subject:
  Within-subjects variances the same
  First level design the same (e.g. number of trials)
Other cases: summary statistics approach is robust against typical violations.
  Simple group fMRI modeling and inference. Mumford & Nichols. NeuroImage, 2009.
Mixed-effects and fMRI studies. Friston et al., NeuroImage, 2005.
Statistical Parametric Mapping: The Analysis of Functional Brain Images. Elsevier, 2007.
Notes: Might use a hierarchical model in epilepsy research where number of seizures is not under experimental control and is highly variable over subjects.
Balanced designs

## Slide 46
ANOVA & non-sphericity
One effect per subject:
  Summary statistics approach
  One-sample t-test at the second level
More than one effect per subject or multiple groups:
  Non-sphericity modelling
  Covariance components and ReML

## Slide 47
Summary
Group Inference usually proceeds with RFX analysis, not FFX. Group effects are compared to between rather than within subject variability.
Hierarchical models provide a gold-standard for RFX analysis but are computationally intensive.
Summary statistics approach is a robust method for RFX group analysis.
Can also use ‘ANOVA’ or ‘ANOVA within subject’ at second level for inference about multiple experimental conditions or multiple groups.

## Slide 48
One-sample t-test
Two-sample t-test
Paired t-test
One-way ANOVA
One-way ANOVA within-subject
Full Factorial
Flexible Factorial
Flexible Factorial

## Slide 49: 2x2 factorial design
A1
A2
B1
B2
A
B
1
2
Color
Shape
Main effect of Shape:
(A1+A2) – (B1+B2) : 1 1 -1 -1
Main effect of Color:
(A1+B1) – (A2+B2) : 1 -1 1 -1
Interaction Shape x Color:
(A1-B1) – (A2-B2) : 1 -1 -1 1

## Slide 50: 2x3 factorial design
Main effect of Shape:
(A1+A2+A3) – (B1+B2+B3) : 1 1 1 -1 -1 -1
Main effect of Color:
(A1+B1) – (A2+B2) : 1 -1 0 1 -1 0
(A2+B2) – (A3+B3) : 0 1 -1 0 1 -1
(A1+B1) – (A3+B3) : 1 0 -1 1 0 -1
Interaction Shape x Color:
(A1-B1) – (A2-B2) : 1 -1 0 -1 1 0
(A2-B2) – (A3-B3) : 0 1 -1 0 -1 1
(A1-B1) – (A3-B3) : 1 0 -1 -1 0 1
A
B
1
2
Color
Shape
3
A1
A2
A3
B1
B2
B3