## Slide 1: fMRI Preprocessing John Ashburner

## Slide 2: Contents
Preliminaries
  Rigid-Body and Affine Transformations
  Optimisation and Objective Functions
  Transformations and Interpolation
Within Subject: Realignment & Coregistration
Between Subject: Spatial Normalisation & Smoothing

## Slide 3: Rigid-Body Transformations
Assume that brain of the same subject doesn’t change shape or size in the scanner.
  Head can move, but remains the same shape and size.
  Some exceptions:
    Image distortions.
    Brain slops about slightly because of gravity.
    Brain growth or atrophy over time.
If the subject’s head moves, we need to correct the images.
  Do this by image registration.

## Slide 4: Image Registration
Two components:
Registration - i.e. Optimise the parameters that describe a spatial transformation between the source and reference images
Transformation - i.e. Re-sample according to the determined transformation parameters

## Slide 5: 2D Affine Transforms
Translations by tx and ty
  x1 = x0 + tx
  y1 = y0 + ty
Rotation around the origin by  radians
  x1 = cos() x0 + sin() y0
  y1 = -sin() x0 + cos() y0
Zooms by sx and sy
  x1 = sx x0
  y1 = sy y0
Shear
  x1 = x0 + h y0
  y1 = y0

## Slide 6: 2D Affine Transforms
Translations by tx and ty
  x1 = 1 x0 + 0 y0 + tx
  y1 = 0 x0 + 1 y0 + ty
Rotation around the origin by  radians
  x1 = cos() x0 + sin() y0 + 0
  y1 = -sin() x0 + cos() y0 + 0
Zooms by sx and sy:
  x1 = sx x0 + 0 y0 + 0
  y1 = 0 x0 + sy y0 + 0
Shear
  x1 = 1 x0 + h y0 + 0
  y1 = 0 x0 + 1 y0 + 0

## Slide 7: 3D Rigid-body Transformations
A 3D rigid body transform is defined by:
  3 translations - in X, Y & Z directions
  3 rotations - about X, Y & Z axes
The order of the operations matters
Translations
Pitch
about x axis
Roll
about y axis
Yaw
about z axis

## Slide 8: Voxel-to-world Transforms
Affine transform associated with each image
  Maps from voxels (x=1..nx, y=1..ny, z=1..nz) to some world co-ordinate system. e.g.,
    Scanner co-ordinates - images from DICOM toolbox
    T&T/MNI coordinates - spatially normalised
Registering image B (source) to image A (target) will update B’s voxel-to-world mapping
  Mapping from voxels in A to voxels in B is by
    A-to-world using MA, then world-to-B using MB-1
    MB-1 MA

## Slide 9: Left- and Right-handed Coordinate Systems
NIfTI format files are stored in either a left- or right-handed system
  Indicated in the header
Talairach & Tournoux uses a right-handed system
Mapping between them sometimes requires a flip
  Affine transform has a negative determinant

## Slide 10: Optimisation
Image registration is done by optimisation.
Optimisation involves finding some “best” parameters according to an “objective function”, which is either minimised or maximised
The “objective function” is often related to a probability based on some model
Value of parameter
Objective function
Most probable solution (global optimum)
Local optimum
Local optimum

## Slide 11: Objective Functions
Intra-modal
  Mean squared difference (minimise)
  Normalised cross correlation (maximise)
Inter-modal (or intra-modal)
  Mutual information (maximise)
  Normalised mutual information (maximise)
  Entropy correlation coefficient (maximise)

## Slide 12: Simple Interpolation
Nearest neighbour
  Take the value of the closest voxel
Tri-linear
  Just a weighted average of the neighbouring voxels
  f5 = f1 x2 + f2 x1
  f6 = f3 x2 + f4 x1
  f7 = f5 y2 + f6 y1

## Slide 13: B-spline Interpolation
B-splines are piecewise polynomials
A continuous function is represented by a linear combination of basis functions
2D B-spline basis functions of degrees 0, 1, 2 and 3
Nearest neighbour and trilinear interpolation are the same as B-spline interpolation with degrees 0 and 1.

## Slide 14: Contents
Preliminaries
Within Subject: Realignment & Coregistration
  Realignment by minimising mean-squared difference
  Residual artifacts and distortion correction
  Coregistration by maximising mutual information
Between Subject: Spatial Normalisation & Smoothing

## Slide 15: Pre-processing Overview
fMRI time-series
Motion Correct
Anatomical MRI
Coregister
Deformation
Estimate Spatial Norm
Spatially normalised
Smooth
Smoothed
Statistics or whatever
Template

## Slide 16: Mean-squared Difference
Minimising mean-squared difference works for intra-modal registration (realignment)
Simple relationship between intensities in one image, versus those in the other
  Assumes normally distributed differences

## Slide 17: Residual Errors from aligned fMRI
Re-sampling can introduce interpolation errors
  especially tri-linear interpolation
Gaps between slices can cause aliasing artefacts
Slices are not acquired simultaneously
  rapid movements not accounted for by rigid body model
Image artefacts may not move according to a rigid body model
  image distortion
  image dropout
  Nyquist ghost
Functions of the estimated motion parameters can be modelled as confounds in subsequent analyses

## Slide 18: Movement by Distortion Interaction of fMRI
Subject disrupts B0 field, rendering it inhomogeneous
  distortions in phase-encode direction
Subject moves during EPI time series
Distortions vary with subject orientation
  shape varies

## Slide 19: Movement by distortion interaction

## Slide 20: Correcting for distortion changes using Unwarp
Estimate movement parameters.
Estimate new distortion fields for each image:
estimate rate of change of field with respect to the current estimate of movement parameters in pitch and roll.
Estimate reference from mean of all scans.
Unwarp time series.

+
Andersson et al, 2001

## Slide 21
Inter-modal registration.
Match images from same subject but different modalities:
  anatomical localisation of single subject activations
  achieve more precise spatial normalisation of functional image using anatomical image.
Coregistration

## Slide 22: Coregistration maximises Mutual Information
Used for between-modality registration
Derived from joint histograms
MI= ab P(a,b) log2 [P(a,b)/( P(a) P(b) )]
  Related to entropy: MI = -H(a,b) + H(a) + H(b)
      Where H(a) = -a P(a) log2P(a) and H(a,b) = -a P(a,b) log2P(a,b)

## Slide 23: Contents
Preliminaries
Within Subject: Realignment & Coregistration
Between Subject: Spatial Normalisation & Smoothing
  Segmentation for spatial normalisation
    More about this in the afternoon
  Smoothing

## Slide 24: Pre-processing Overview
fMRI time-series
Motion Correct
Anatomical MRI
Coregister
Deformation
Estimate Spatial Norm
Spatially normalised
Smooth
Smoothed
Statistics or whatever
Template

## Slide 25: Alternative Pipeline
fMRI time-series
Motion Correct
Deformation
Estimate Spatial Norm
Spatially normalised
Smooth
Smoothed
Statistics or whatever
Template

## Slide 26: Spatial Normalisation
Brains of different subjects vary in shape and size.
Need to bring them all into a common anatomical space.
  Examine homologous regions across subjects
    Improve anatomical specificity
    Improve sensitivity
  Report findings in a common anatomical space (eg MNI space)
In SPM, alignment is achieved by matching grey matter with grey matter and white matter with white matter.
  Need to segment.

## Slide 27: Segmentation
Segmentation in SPM8 also estimates a spatial transformation that can be used for spatially normalising images.
It uses a generative model, which involves:
  Mixture of Gaussians (MOG)
  Bias Correction Component
  Warping (Non-linear Registration) Component

## Slide 28: Tissue Probability Maps
Tissue probability maps (TPMs) are used instead of the proportion of voxels in each Gaussian as the prior.
ICBM Tissue Probabilistic Atlases. These tissue probability maps are kindly provided by the International Consortium for Brain Mapping, John C. Mazziotta and Arthur W. Toga.

## Slide 29: Deforming the Tissue Probability Maps
Tissue probability images are deformed so that they can be overlaid on top of the image to segment.

## Slide 30
Evaluations of nonlinear registration algorithms

## Slide 31: Smooth
Before convolution
Convolved with a circle
Convolved with a Gaussian
Blurring is done by convolution.
Each voxel after smoothing effectively becomes the result of applying a weighted region of interest (ROI).

## Slide 32: References
Friston et al. Spatial registration and normalisation of images. Human Brain Mapping 3:165-189 (1995).
Collignon et al. Automated multi-modality image registration based on information theory. IPMI’95 pp 263-274 (1995).
Thévenaz et al. Interpolation revisited. IEEE Trans. Med. Imaging 19:739-758 (2000).
Andersson et al. Modeling geometric deformations in EPI time series. Neuroimage 13:903-919 (2001).
Ashburner & Friston. Unified Segmentation. NeuroImage 26:839-851 (2005).
Klein et al. Evaluation of 14 nonlinear deformation algorithms applied to human brain MRI registration. NeuroImage 46(3):786-802 (2009).