## Slide 1: SPM Course May 2012 Segmentation and Voxel-Based Morphometry
Ged Ridgway
With thanks to John Ashburner
and the FIL Methods Group

## Slide 2: Overview
Unified segmentation
Voxel-based morphometry (VBM)
Spatial normalisation with Dartel

## Slide 3: Segmentation into principal tissue types
High-resolution MRI reveals fine structural detail in the brain, but not all of it reliable or interesting
  Noise, intensity-inhomogeneity, vasculature, …
MR intensity is usually not quantitative (cf. relaxometry)
  fMRI time-series allow signal changes to be analysed statistically, compared to baseline or global values
Regional volumes of the three main tissue types: gray matter, white matter and CSF, are well-defined and potentially very interesting

## Slide 4: Summary of unified segmentation
Unifies tissue segmentation and spatial normalisation
  Principled Bayesian formulation: probabilistic generative model
Gaussian mixture model with deformable tissue prior probability maps (from segmentations in MNI space)
  The inverse of the transformation that aligns the TPMs can be used to normalise the original image to standard space
  [Or the rigid component can be used to initialise Dartel/GS]
Intensity non-uniformity (bias) is included in the model

## Slide 5: Tissue intensity distributions (T1-w MRI)

## Slide 6: Gaussian mixture model (GMM or MoG)
Classification is based on a Mixture of Gaussians (MoG) model fitted to the intensity probability density (histogram)
Image Intensity
Frequency

## Slide 7: Non-Gaussian Intensity Distributions
Multiple Gaussians per tissue class allow non-Gaussian intensity distributions to be modelled.
  E.g. accounting for partial volume effects

## Slide 8: Modelling inhomogeneity
MR images are corrupted by spatially smooth intensity variations (worse at high field strength)
A multiplicative bias correction field is modelled as a linear combination of basis functions.
Corrupted image
Corrected image
Bias Field

## Slide 9: TPMs – Tissue prior probability maps
Each TPM indicates the prior probability for a particular tissue at each point in MNI space
  Fraction of occurrences in previous segmentations
TPMs are warped to match the subject
  The inverse transform normalises to MNI space

## Slide 10: Limitations of the current model
Assumes that the brain consists of only the tissues modelled by the TPMs
  No spatial knowledge of lesions (stroke, tumours, etc)
Prior probability model is based on relatively young and healthy brains
  Less appropriate for subjects outside this population
Needs reasonable quality images to work with
  No severe artefacts
  Good separation of intensities
  Good initial alignment with TPMs...

## Slide 11: Possible extensions
Deeper Bayesian philosophy
  E.g. priors over means and variances
  Marginalisation of nuisance variables
  Model comparison, e.g. for numbers of Gaussians
Groupwise model (enormous!)
Combination with DARTEL (see later)
More tissue priors e.g. separating cortical and deep grey
Imaging physics
  See Fischl et al. (2004), as cited in A&F (2005) introduction

## Slide 12: Overview
Unified segmentation
Voxel-based morphometry (VBM)
Spatial normalisation with Dartel

## Slide 13: Computational neuroanatomy
Quantitative analysis of variability in biological shape
  Can be univariate or multivariate, inferential or predictive
Example applications
  Distinguish groups (e.g schizophrenics from healthy controls)
  Model changes (e.g. in development or aging)
  Characterise plasticity, e.g. when learning new skills
  Find structural correlates (scores, traits, genetics, etc.)
  Differentiate degenerative disease from healthy aging
    Evaluate subjects on drug treatments versus placebo

## Slide 14: Voxel-Based Morphometry
Most widely used method for computational anatomy
VBM is essentially Statistical Parametric Mapping of regional segmented tissue density or volume
The exact interpretation of gray matter density or volume is complicated, and depends on the preprocessing steps used
  It is not interpretable as neuronal packing density or other cytoarchitectonic tissue properties
  The hope is that changes in these microscopic properties may lead to macro- or mesoscopic VBM-detectable differences

## Slide 15: VBM methods overview
Unified segmentation and spatial normalisation
  More flexible groupwise normalisation using DARTEL
[Optional] modulation with Jacobian determinant
Optional computation of tissue totals/globals
Gaussian smoothing
Voxel-wise statistical analysis

## Slide 16: VBM in pictures
Segment
Normalise

## Slide 17: VBM in pictures
Segment
Normalise
Modulate
Smooth

## Slide 18: VBM in pictures
Segment
Normalise
Modulate
Smooth
Voxel-wise statistics

## Slide 19: VBM in pictures
Segment
Normalise
Modulate
Smooth
Voxel-wise statistics
beta_0001
con_0001
ResMS
spmT_0001
FWE < 0.05

## Slide 20: VBM Subtleties
Whether to modulate
How much to smooth
Interpreting results
Adjusting for total GM or Intracranial Volume
Statistical validity

## Slide 21: Modulation
Multiplication of the warped (normalised) tissue intensities so that their regional or global volume is preserved
  Can detect differences in completely registered areas
Otherwise, we preserve concentrations, and are detecting mesoscopic effects that remain after approximate registration has removed the macroscopic effects
  Flexible (not necessarily “perfect”) registration may not leave any such differences
1 1
2/3 1/3 1/3 2/3
1 1 1 1
Native
intensity = tissue density
Modulated
Unmodulated
Notes: Clarify, modulation not a step (as spm2) but an option in the segment and the normalise GUIs

## Slide 22: Modulation tutorial
http://tinyurl.com/ModulationTutorial
X = x2
X’ = dX/dx = 2x
X’(2.5) = 5
Red area = Square – cyan – magenta – green = pr+ps+qr+qs – 2qr – qs – pr = ps – qr

## Slide 23: Smoothing
The analysis will be most sensitive to effects that match the shape and size of the kernel
The data will be more Gaussian and closer to a continuous random field for larger kernels
Results will be rough and noise-like if too little smoothing is used
Too much will lead to distributed, indistinct blobs

## Slide 24: Smoothing
Between 7 and 14mm is probably reasonable
  (DARTEL’s greater precision allows less smoothing)
  The results below show two fairly extreme choices, 5mm on the left, and 16mm, right

## Slide 25: Interpreting findings
Thickening
Thinning
Folding
Mis-classify
Mis-classify
Mis-register
Mis-register

## Slide 26: “Globals” for VBM
Shape is really a multivariate concept
  Dependencies among volumes in different regions
SPM is mass univariate
  Combining voxel-wise information with “global” integrated tissue volume provides a compromise
  Using either ANCOVA or proportional scaling
(ii) is globally thicker, but locally thinner than (i) – either of these effects may be of interest to us.
Fig. from: Voxel-based morphometry of the human brain… Mechelli, Price, Friston and Ashburner. Current Medical Imaging Reviews 1(2), 2005.
Notes: Note globals don’t help distinguish the thickened or folded cortex...

## Slide 27: Total Intracranial Volume (TIV/ICV)
“Global” integrated tissue volume may be correlated with interesting regional effects
  Correcting for globals in this case may overly reduce sensitivity to local differences
  Total intracranial volume integrates GM, WM and CSF, or attempts to measure the skull-volume directly
    Not sensitive to global reduction of GM+WM (cancelled out by CSF expansion – skull is fixed!)
  Correcting for TIV in VBM statistics may give more powerful and/or more interpretable results
    See e.g. Barnes et al., (2010), NeuroImage 53(4):1244-55

## Slide 28: VBM’s statistical validity
Residuals are not normally distributed
  Little impact for comparing reasonably sized groups
  Potentially problematic for comparing single subjects or tiny patient groups with a larger control group
  Mitigate with large amounts of smoothing
  Or use nonparametric tests that make fewer assumptions, e.g. permutation testing with SnPM
Smoothness is not spatially stationary
  Bigger blobs expected by chance in smoother regions
  NS toolbox http://www.fil.ion.ucl.ac.uk/spm/ext/#NS
Voxel-wise FDR is common, but not recommended

## Slide 29: Longitudinal VBM
The simplest method for longitudinal VBM is to use cross-sectional preprocessing, but longitudinal statistics
  Standard preprocessing not optimal, but unbiased
  Non-longitudinal statistics would be severely biased
    (Estimates of standard errors would be too small)
  Simplest longitudinal statistical analysis: two-stage summary statistic approach (common in fMRI)
    Within subject longitudinal differences or beta estimates from linear regressions against time

## Slide 30: Longitudinal VBM variations
Intra-subject registration over time is much more accurate than inter-subject normalisation
A simple approach is to apply one set of normalisation parameters (e.g. Estimated from baseline images) to both baseline and repeat(s)
  Draganski et al (2004) Nature 427: 311-312
More sophisticated approaches use nonlinear within-subject registration, e.g. with HDW or new toolbox
  E.g. Kipps et al (2005) JNNP 76:650
  Beware of bias from asymmetries! (Thomas et al 2009) doi:10.1016/j.neuroimage.2009.05.097

## Slide 31: Overview
Unified segmentation
Voxel-based morphometry (VBM)
Spatial normalisation with Dartel

## Slide 32: Spatial normalisation with DARTEL
VBM is crucially dependent on registration performance
  Limited flexibility (low DoF) registration has been criticised
  Inverse transformations are useful, but not always well-defined
  More flexible registration requires careful modelling and regularisation (prior belief about reasonable warping)
  MNI/ICBM templates/priors are not universally representative
The DARTEL toolbox combines several methodological advances to address these limitations
Evaluations show DARTEL performs at state-of-the art
  E.g. Klein et al., (2009) NeuroImage 46(3):786-802 …

## Slide 33
Part of Fig.1 in Klein et al.
Part of Fig.5 in Klein et al.
Notes: Recent papers comparing different approaches have favoured more flexible methods
DARTEL usually outperforms DCT normalisation
  Also comparable to the best algorithms from other software packages (though note that DARTEL and others have many tunable parameters...)

## Slide 34: DARTEL Transformations
Estimate (and regularise) a flow u
  (think syrup rather than elastic)
  3 (x,y,z) parameters per 1.5mm3 voxel
  10^6 degrees of freedom vs. 10^3 DF for old discrete cosine basis functions
φ(0)(x) = x
φ(1)(x) = ∫ u(φ(t)(x))dt
Scaling and squaring is used to generate deformations
Inverse simply integrates -u
t=0
1

## Slide 35: DARTEL objective function
Likelihood component (matching)
  Specific for matching tissue segments to their mean
  Multinomial distribution (cf. Gaussian)
Prior component (regularisation)
  A measure of deformation (flow) roughness = ½uTHu
Need to choose H and a balance between the two terms
  Defaults usually work well (e.g. even for AD)
  Though note that changing models (priors) can change results

## Slide 36: Simultaneous registration of GM to GM and WM to WM, for a group of subjects
Grey matter
White matter
Grey matter
White matter
Grey matter
White matter
Grey matter
White matter
Grey matter
White matter
Template
Subject 1
Subject 2
Subject 3
Subject 4

## Slide 37: Example geodesic shape average
Linear Average
Average on Riemannian manifold
(Not on Riemannian manifold)
Uses average flow field

## Slide 38: DARTEL average template evolution
Rigid average (Template_0)
Average of mwc1 using segment/DCT
Template
6
Template
1
Notes: 60 images from OASIS cross-sectional data (as in VBM practical)

## Slide 41: Summary
VBM performs voxel-wise statistical analysis on smoothed (modulated) normalised tissue segments
SPM8 performs segmentation and spatial normalisation in a unified generative model
  Based on Gaussian mixture modelling, with DCT-warped spatial priors, and multiplicative bias field
  The new segment toolbox includes non-brain priors and more flexible/precise warping of them
Subsequent (currently non-unified) use of DARTEL improves normalisation for VBM
  And probably also fMRI...

## Slide 42: Extra material

## Slide 43: Preprocessing overview
fMRI time-series
Motion corrected
Mean functional
REALIGN
COREG
Anatomical MRI
SEGMENT
NORM WRITE
SMOOTH
TPMs
ANALYSIS
Input
Output
Segmentation
Transformation
(seg_sn.mat)
Kernel
(Headers changed)
MNI Space

## Slide 44: Preprocessing with Dartel
fMRI time-series
Motion corrected
Mean functional
REALIGN
COREG
Anatomical MRI
SEGMENT
DARTEL NORM 2 MNI & SMOOTH
TPMs
(Headers changed)
ANALYSIS
DARTEL CREATE TEMPLATE
...

## Slide 45: Mathematical advances in computational anatomy
VBM is well-suited to find focal volumetric differences
Assumes independence among voxels
  Not very biologically plausible
  But shows differences that are easy to interpret
Some anatomical differences can not be localised
  Need multivariate models
  Differences in terms of proportions among measurements
  Where would the difference between male and female faces be localised?

## Slide 46: Mathematical advances in computational anatomy
In theory, assumptions about structural covariance among brain regions are more biologically plausible
  Form influenced by spatio-temporal modes of gene expression
Empirical evidence, e.g.
  Mechelli, Friston, Frackowiak & Price. Structural covariance in the human cortex. Journal of Neuroscience 25:8303-10 (2005)
Recent introductory review:
  Ashburner & Klöppel. “Multivariate models of inter-subject anatomical variability”. NeuroImage 56(2):422-439 (2011)

## Slide 47: Summary of extra material
VBM uses the machinery of SPM to localise patterns in regional volumetric variation
  Use of “globals” as covariates is a step towards multivariate modelling of volume and shape
More advanced approaches typically benefit from the same preprocessing methods
  New segmentation and DARTEL close to state of the art
  Though possibly little or no smoothing
Elegant mathematics related to transformations (diffeomorphism group with Riemannian metric)
VBM – easier interpretation – complementary role

## Slide 48: Historical bibliography of VBM
A Voxel-Based Method for the Statistical Analysis of Gray and White Matter Density… Wright, McGuire, Poline, Travere, Murrary, Frith, Frackowiak and Friston (1995 (!)) NeuroImage 2(4)
  Rigid reorientation (by eye), semi-automatic scalp editing and segmentation, 8mm smoothing, SPM statistics, global covars.
Voxel-Based Morphometry – The Methods. Ashburner and Friston (2000) NeuroImage 11(6 pt.1)
  Non-linear spatial normalisation, automatic segmentation
  Thorough consideration of assumptions and confounds

## Slide 49: Historical bibliography of VBM
A Voxel-Based Morphometric Study of Ageing… Good, Johnsrude, Ashburner, Henson and Friston (2001) NeuroImage 14(1)
  Optimised GM-normalisation (“a half-baked procedure”)
Unified Segmentation. Ashburner and Friston (2005) NeuroImage 26(3)
  Principled generative model for segmentation using deformable priors
A Fast Diffeomorphic Image Registration Algorithm. Ashburner (2007) Neuroimage 38(1)
  Large deformation normalisation
Computing average shaped tissue probability templates. Ashburner & Friston (2009) NeuroImage 45(2): 333-341