## Slide 1: M/EEG pre-processing
Holly Rossiter
Wellcome Trust Centre for Neuroimaging
UCL Institute of Neurology

## Slide 2: Steps to cover
Conversion
Filtering
Downsampling
Epoching
Re-referencing for EEG
Artefacts
Averaging
Coregistration
Generating scalp x time images
Time-frequency analysis

## Slide 3
What do we need?
M/EEG signals
Time axis
(sampling frequency and onset)
Sensor locations
Events
Possible source
of artefact
Hans Berger
1873-1941

## Slide 4
~300 sensors
<128 electrodes

## Slide 5
resting state
falling asleep
sleep
deep sleep
coma
1 sec
50 uV
Evoked response vs. spontaneous activity
post-stim
pre-stim
evoked response
ongoing rhythms
Averaging
active
awake state

## Slide 6
Clarification of terms – SPM speak
GUI
Script
Batch
Notes: In each script for spm functions, there is a help section at the top or you can type help function in to the command line to get the same information.

## Slide 7
As opposed to GUI
  - it is easy to reproduce analyses, apply them to different datasets and make modifications.
  - removing interactive GUI elements from the code makes it cleaner and easier to maintain.
As opposed to script
  complex pipelines can be built without programming expertise
  saved pipelines can be examined without deciphering other people’s code
  batch provides uniform interface for scripting to different parts of SPM code.
Disadvantages of batch
  there is no step-by-step guiding of the user
  the need to prepare all the inputs in advance makes some of the operations less intuitive and requires getting used to.
Why batch?
Notes: Mention fieldtrip here and that some scripts run by spm are from fieldtrip and they work very well together – however fieldtrip is generally much more command line and does not have a graphical user interface so not easy for beginners but can use for specific functions once you become more experienced with programming. Basically they work very well together.

## Slide 8
Raw data with triggers

## Slide 10: Now lets take a step back

## Slide 11: Steps to cover
Conversion
Filtering
Downsampling
Epoching
Re-referencing for EEG
Artefacts
Averaging
Coregistration
Generating scalp x time images
Time-frequency analysis
spm_eeg_convert
Notes: Every time you run a preprocessing step, it will save a new dataset with a specific letter prepending it for example convert adds spmeeg_ to the front of the filename and filtering adds an f so you can track what steps you have done from the letters of the filename and you can also go back to previous steps and rerun things.

## Slide 12
Arbitrary
ASCII
Matlab
MEG
CTF
Neuromag
BTi-4D
Yokogawa
EEG
EEGLAB
Biosemi
Brainvision
Neuroscan
EGI
ANT
SPM5
…
Biosig
Conversion
Fieldtrip
raw
timelock
freq
Convert button
(fileio)
spm_eeg_convert
spm_eeg_ft2spm
GUI
script
SPM dataset
*.dat – binary data file
*.mat – header file
Prepare
(Import from workspace)
+
Reviewing tool

## Slide 13
The *.mat file contains a struct, named D, which is converted to an meeg object by spm_eeg_load.
The *.dat file contains the data and is memory-mapped and linked to the object in order to save memory.
Expert’s corner

## Slide 14: Conversion
In GUI you have the option to define settings or ‘just read’
Settings to define…
  Continuous or epoched
  Which channels to include
  etc

## Slide 15: Steps to cover
Conversion
Filtering
Downsampling
Epoching
Re-referencing for EEG
Artefacts
Averaging
Coregistration
Generating scalp x time images
Time-frequency analysis
spm_eeg_filter

## Slide 16
Filtering
High-pass – remove the DC offset and slow trends in the data.
Low-pass – remove high-frequency noise. Similar to smoothing.
Notch (band-stop) – remove artefacts limited in frequency, most commonly line noise and its harmonics.
Band-pass – focus on the frequency of interest and remove the rest. More suitable for relatively narrow frequency ranges.
Notes: Cannot use frequencies above the Nyquist frequency (half the sampling rate)

## Slide 17
Unfiltered
5Hz high-pass
10Hz high-pass
45Hz low-pass
20Hz low-pass
Filtering - examples
10Hz low-pass
Notes: Good idea to start with wide frequency band and then perhaps specify smaller frequency band at later stages once you’ve explored your data

## Slide 18: Steps to cover
Conversion
Filtering
Downsampling
Epoching
Re-referencing for EEG
Artefacts
Averaging
Coregistration
Generating scalp x time images
Time-frequency analysis
spm_eeg_downsample

## Slide 19: Steps to cover
Conversion
Filtering
Downsampling
Epoching
Re-referencing for EEG
Artefacts
Averaging
Coregistration
Generating scalp x time images
Time-frequency analysis
spm_eeg_epochs

## Slide 20
Epoching
Data visualization:
Scroll through trials
Important to understand triggers in data when recording!

## Slide 21
Epoching
Definition: Cutting segments around events.
Need to know:
What happens (event type, event value)
When it happens (time of the events)
Need to define:
Segment borders
Trial type (can be different triggers => single trial type)
Shift of time zero of the trial with respect to the trigger (no shift by default).
Note:
SPM only supports fixed length trials
The epoching function also performs baseline correction (using negative times as the baseline). You can also do this separately.

## Slide 22: Steps to cover
Conversion
Filtering
Downsampling
Epoching
Re-referencing for EEG
Artefacts
Averaging
Coregistration
Generating scalp x time images
Time-frequency analysis
spm_eeg_montage

## Slide 23
Average reference
EEG – re-referencing
Notes: Potential difference between 2 points. Can use somewhere on head like nose or mastoid or average across all channels as reference – compromise – bad if few channels might be harder to see subtle changes
Can take most positive channel and make this ref so all else is negative or vice versa – if you then do stats – you can sensitise to particular phenomena.

## Slide 24
Re-referencing can be used to sensitize sensor level analysis to particular sources (at the expense of other sources).
For source reconstruction and DCM it is necessary to specify the referencing of the data. This can be done via the ‘Prepare’ tool.
Re-referencing in SPM is done by the Montage function that can apply any linear weighting to the channels and has a wider range of applications.
EEG – re-referencing
Notes: What else is montage used for? ICA components/source extraction

## Slide 25: Steps to cover
Conversion
Filtering
Downsampling
Epoching
Re-referencing for EEG
Artefacts
Averaging
Coregistration
Generating scalp x time images
Time-frequency analysis
spm_eeg_artefact

## Slide 26
EEG
MEG
Planar
Eye blink
Artefacts

## Slide 27: Examples in MEG data muscle artefact, eye blink, sensor jumps

## Slide 28
Artefacts
SPM has an extendable artefact detection function where plug-ins implementing different detection methods can be applied to subsets of channels.
A variety of methods are implemented including, amplitude thresholding, jump detection, flat segment detection, ECG and eye blink detection.
In addition, topography-based artefact correction method is available (in MEEGtools toolbox).

## Slide 29
New in SPM12
It is now possible to mark artefacts in continuous data
Marked artefacts are saved as events which are carried over with subsequent processing. So it is possible e.g. to mark artefacts before filtering and keep for later.
Marked artefacts can be used for trial rejection at a later stage (‘Reject based on events’)
time (s)
Channels
>> imagesc(D.badsamples(D.indchantype('EEG'), ':', 1))

## Slide 30: Steps to cover
Conversion
Filtering
Downsampling
Epoching
Re-referencing for EEG
Artefacts
Averaging
Coregistration
Generating scalp x time images
Time-frequency analysis
spm_eeg_average

## Slide 31: Averaging across trials

## Slide 32
Kilner, unpublished
Wager et al. Neuroimage, 2005
Robust averaging
Notes: Red is robust, blue is standard

## Slide 33
Robust averaging
Robust averaging is an iterative procedure that computes the mean, down-weights outliers, re-computes the mean etc. until convergence.
It relies on the assumption that for any channel and time point most trials are clean.
The number of trials should be sufficient to get a distribution (at least a few tens).
Robust averaging can be used either in combination with or as an alternative to trial rejection.
Notes: Robust averaging is good for artefact suppression – uses the distribution of data to find outliers (distance from median) and suppress them (downweight them)
Need a good number of trials – need most to be clean
If artefact at same time each trial then this is not good – could use ICA instead

## Slide 34
So that’s how we got to this point
Converted
Filtered
Downsampled
Epoched
Re-referenced for EEG
Removed artefacts
Averaged

## Slide 35
There is no single correct order of steps, but here are some considerations for order choices
  It is better to filter continuous data prior to epoching to avoid filter ringing artefacts in every trial. Alternatively the epochs of interest can be padded with more data and then cropped after filtering.
  It is better to do high-pass filtering or baseline correction before other filtering steps to reduce filter ringing.
  It is convenient to put downsampling early in the pipeline to make the subsequent steps faster.
  SPM only filters channels with physiological data. So the channel types should be set correctly before filtering.
  Some artefacts (e.g. discontinuous jumps or saturations) are more difficult to detect after filtering.
A note about order

## Slide 36: Steps to cover
Conversion
Filtering
Downsampling
Epoching
Re-referencing for EEG
Artefacts
Averaging
Coregistration
Generating scalp x time images
Time-frequency analysis

## Slide 37: 3D Source Reconstruction
Map sensors onto template brain or individual structural MRI
Need template/structural
Need fiducial coordinates if using individual MRI
Need to choose a forward model (e.g. single shell)

## Slide 38: Steps to cover
Conversion
Filtering
Downsampling
Epoching
Re-referencing for EEG
Artefacts
Averaging
Coregistration
Generating scalp x time images
Time-frequency analysis

## Slide 39
Generating time x scalp images
Notes: 3D image mapped over time – create these images and then can run all sorts of stats on them – 4D images
Y axis is time, x axis is first left to right of brain and second anterior to posterior of brain

## Slide 40: Steps to cover
Conversion
Filtering
Downsampling
Epoching
Re-referencing for EEG
Artefacts
Averaging
Coregistration
Generating scalp x time images
Time-frequency analysis
spm_eeg_tf

## Slide 42
Joseph Fourier (1768-1830)
Any complex time series can be broken down into a series of superimposed sinusoids with different frequencies
Fourier analysis

## Slide 43
Original
Different amplitude
Different phase
Fourier analysis

## Slide 44: Time-frequency spectrograms

## Slide 45
Methods of spectral estimation
Morlet 3 cycles
Morlet 5 cycles
Morlet 7 cycles
Morlet 5 cycles
Morlet 7 cycles
Morlet 9 cycles
Boxcar
Hanning
Hillbert transform
Multitaper
Notes: Wavelet is a sine wave multiplied by a gaussian kernel
Aim of tapers is to reduce spectral leakage
Tapering is pulling the data at the edges towards 0 to diminish edge effects
Trade off between temporal and frequency resolution
Boxcar, Hanning taper, Hillbert transform, multitaper
Gaussian is narrower and more curved compared to hanning
Higher freq is more usually broadband – multitapes useful for this
Low freq usually better estimated by single (Hanning) taper
Multitaper good for gamma

## Slide 46
Unweighted averaging
Robust averaging
Robust averaging for TF

## Slide 47
Raw
Diff [-7 -4]s
Log
Rel [-7 -4]s
Rel [-0.5 0.5]s
LogR [-7 -4]s
TF rescaling
Notes: Log = equates different frequencies
Rel = divides everything by the baseline (similar to LogR – like ratio)
Diff = subtracts baseline (doesn’t help with high frequencies)
LogR = log + baseline correction
Using a Diff baseline time window will effect what you see
Be careful of what activity is present in baseline

## Slide 48
Changes to TF data handling in SPM12
TF analysis can be done on continuous data.
Continuous TF data can be filtered, epoched and used as input to convolution modelling.
Notes: Ask Vladimir about this

## Slide 49: Summary
We have covered all these pre-processing steps:
Conversion – Filtering – Downsampling – Epoching - Re-referencing for EEG -
Artefacts – Averaging – Coregistration - Generating scalp x time images -
Time-frequency analysis
From here you can go on to source analysis and stats…

## Slide 50
Thanks to:
Vladimir Litvak
Stefan Kiebel
Jean Daunizeau
Gareth Barnes
James Kilner
Robert Oostenveld
Arnaud Delorme
Laurence Hunt
and all the members of the methods group past and present