## Slide 1: The General Linear Model
Nadège Corbin
Wellcome Trust Centre for Neuroimaging
University College London
SPM fMRI Course
London, May 2018
Thank you to Guillaume Flandin for the slides

## Slide 2
Normalisation
Statistical Parametric Map
Image time-series
Parameter estimates
General Linear Model
Realignment
Smoothing
Design matrix
Anatomical reference
Spatial filter
Statistical Inference
RFT
p <0.05

## Slide 3
Passive word listening
versus rest
7 cycles of
rest and listening
Blocks of 6 scans
with 7 sec TR
Question: Is there a change in the BOLD response between listening and rest?
Stimulus function
One session
A very simple fMRI experiment

## Slide 4
BOLD signal
Time
single voxel
time series
Voxel-wise time series analysis
Model
specification
Parameter
estimation
Hypothesis
Statistic
Time
SPM

## Slide 5
BOLD signal
Time
=
1
2
+
+
error
x1
x2
e
Single voxel regression model

## Slide 6
Mass-univariate analysis: voxel-wise GLM
=
+
y
X
Model is specified by
Design matrix X
Assumptions about e
N: number of scans
p: number of regressors
The design matrix embodies all available knowledge about experimentally controlled factors and potential confounds.

## Slide 7
    one sample t-test
    two sample t-test
    paired t-test
    Analysis of Variance (ANOVA)
    Analysis of Covariance (ANCoVA)
    correlation
    linear regression
    multiple regression
GLM: a flexible framework for parametric analyses

## Slide 8
Parameter estimation
=
+
Objective:
estimate parameters to minimize
Ordinary least squares estimation (OLS) (assuming i.i.d. error):
y
X

## Slide 9
A geometric perspective on the GLM
y
e
Design space defined by X
x1
x2
Smallest errors (shortest error vector)
when e is orthogonal to X
Ordinary Least Squares (OLS)
O

## Slide 10
Problems of this model with fMRI time series
The BOLD response has a delayed and dispersed shape.
The BOLD signal includes substantial amounts of low-frequency noise (eg due to scanner drift).
Due to breathing, heartbeat & unmodeled neuronal activity, the errors are serially correlated. This violates the assumptions of the noise model in the GLM.

## Slide 11
Boynton et al, NeuroImage, 2012.
Scaling
Additivity
Shift invariance
Problem 1: BOLD response
Hemodynamic response function (HRF):
Linear time-invariant (LTI) system:
u(t)
x(t)
hrf(t)
Convolution operator:

## Slide 12
Convolution model of the BOLD response
Convolve stimulus function with a canonical hemodynamic response function (HRF):
 HRF

## Slide 13
blue = data
black = mean + low-frequency drift
green = predicted response, taking into account low-frequency drift
red = predicted response, NOT taking into account low-frequency drift
Problem 2: Low-frequency noise Solution: High pass filtering
discrete cosine transform (DCT) set

## Slide 14
autocovariance
function
Problem 3: Serial correlations
i.i.d:

## Slide 15
Let
Equivalent to the Weighted Least Square (WLS) estimator
Solution : Whitening the data
BUT this requires an estimation of V

## Slide 16
Multiple covariance components
=
1
+ 2
Q1
Q2
Estimation of hyperparameters  with ReML (Restricted Maximum Likelihood).
V
enhanced noise model at voxel i
error covariance components Q and hyperparameters

## Slide 17
The AR(1)+white noise model may not be enough for short TR (<1.5 s)
=
+
+
+
+
V
+ …
The flexibility of the ReML enables the use of any number of components of any shape

## Slide 18: Summary
Mass univariate approach.
Fit GLMs with design matrix, X, to data at different points in space to estimate local effect sizes,
GLM is a very general approach
Hemodynamic Response Function
High pass filtering
Temporal autocorrelation

## Slide 19: A mass-univariate approach
Time
Summary

## Slide 20: Estimation of the parameters
=
noise assumptions:
Pre-whitening:
=
Summary

## Slide 21
Contrasts & statistical parametric maps
Q: activation during listening ?
c = 1 0 0 0 0 0 0 0 0 0 0
Null hypothesis:

## Slide 22: References
Statistical parametric maps in functional imaging: a general linear approach, K.J. Friston et al, Human Brain Mapping, 1995.
Analysis of fMRI time-series revisited – again, K.J. Worsley and K.J. Friston, NeuroImage, 1995.
The general linear model and fMRI: Does love last forever?, J.-B. Poline and M. Brett, NeuroImage, 2012.
Linear systems analysis of the fMRI signal, G.M. Boynton et al, NeuroImage, 2012.